# REPORT ON
DEVELOPMENT OF CHRONICALLY FLOOD
AFFECTED AREAS

# NATIONAL COMMITTEE
ON
THE DEVELOPMENT OF BACKWARD AREAS

PLANNING COMMISSION
GOVERNMENT OF INDIA
NEW DELHI
NOVEMBER, 1981

# REPORT ON

# DEVELOPMENT OF CHRONICALLY FLOOD AFFECTED AREAS

# Contents

| SI. No. | Pages |
| --- | --- |
| Summary of Conclusions and Recommendations | (i)-(v) |
| 1. Introduction | 1—2 |
| 2. Identification of Chronically Flood Affected Areas and Strategy towards Development | 3—27 |
| 3. Cropping Strategy | 28—31 |
| 4. Irrigation Strategy | 32—33 |
| 5. Measures to Mitigate Flood Damages | 34—40 |
| ANNEXURES |  |
| Chapter 2 |  |
| Annexure 2.1 Flood Damages in India During 1953 to 1980 |  |
| Annexure 2.2 Frequency and incidence of Flooding in some rivers of Orissa | 10—21 |
| Annexure 2.3 Incidence of earliest, latest and latast but one floods in major rivers of UP during last years | 22—24 |
| Annexure 2.4 Flood period in different areas in West Bengal | 25—27 |
| Chapter 5 |  |
| Annexure 5.1 Extracts of the Report on Irrigation, Drainage and Water Management in China by Shri R.S. Saksena | 40 |

# SUMMARY OF CONCLUSIONS AND RECOMMENDATIONS

# I. INTRODUCTION

1. Chronically    flood    affected    areas    should    be treated as backward areas, and special measures instituted for dealing with their problems, and promoting their economic development.

(Para 1.1)

2. It is necessary to identify the ameliorating steps necessary for the development of the affected areas where damage is caused by natural havoc and is in the flood plains where neither any embankment exists nor are provided in the Master Plan. This is where nature's direct havoc on the economy is felt and this havoc, if chronic, creates the problems of backwardness.

(Para 1.11)

# II. IDENTIFICATION OF CHRONICALLY FLOOD AFFCTED AREAS    AND STRATEGY TOWARDS DEVELOPMENT

3. The following criteria should be used for identification of the chronically flood prone areas:

(i) flood frequency of at least once in three years,

(ii) flood duration of at least 7 days period at a stretch,

(iii) flood depth of more than the standing paddy at that time, and

(iv) flash floods with strong current liable to uproot plants even if the duration is less than 7 days.

(Para 2.4)

4. In all flood plains, one single Department must be designated as the Department to maintain sufficient hydraulic data. It is only this data which would enable a demarcation of the chonically flood affected areas and the nature and the change in such areas over time.

(Para 2.5)

5. In all the blocks affected by floods, the exercise to refine the identification of chronically flood affected areas requiring amelioration may be done within the next two years so    that a realistic and    satisfactory ameliorative programme can be introduced.

(Para 2.8)

6. Unlike the demarcation area of a block which the committee has deemed useful for planning in its reports already submitted, the area considered appropriate for the present report, for obvious reasons, is a water basin or sub-basin. 				(Para 2.9)

7. Measures to mitigate flood losses need to be part of a comprehensive   scheme   where in modification of floods, reduced damage    susceptibilities of infrastructure and property are looked at an integrated fashion.

(Para 2.15)

8. For developmental    purposes  it should not be difficult for a project   approach    to be implemented covering part areas of the blocks so long as they fall in a basin or sub-basin.

(Para 2.16)

9. Crop    damage is    one of the    worst    damages caused  in  floods.  An  appropriate  cropping  strategy and other steps have therefore to be adopted in these areas-   The obvious pathways would be to popularise suitable flood escaping or flood tolerant cropping system  or  intensive  crop production with  irrigation  in the flood free months there. The Committee considers that maximum utilisation of the water resources available in these    areas    and    introduction of suitable cropping strategies would be the most important steps for the development of these areas.

(Para 2.17)

10. Regarding    the    damage    caused   to   houses, property     and infrastructure, strengthening of house structure, raising the level of whole villages or providing ring bunds around villages have been considered as possible alternatives. Each of these alternatives has positive and negative aspects; yet the fact remains that something has got to be done to provide protection to the human settlement.

(Para 2.18)

11. The committee would also like to emphasise the importance of pre-disaster preparedness measures since they can change a major disaster into a minor one and mitigate the suffering of those likely to be affected.

(Para 2.19)

12. The Meteorological Department is reported to have drawn up a comprehensive scheme for improving meteorological telecommunication net work for collection of data and its prompt dissemination to the appropriate  quarters.  The  Committee would  suggest early decision on these proposals.

(Para 2.24)

13. The Central Flood Forecasting Organisation is maintaining a net-work of observation stations where gauges have been    installed to Record River    flows, sediment discharge etc.  The  Rashtriya  Barh   Ayog have pointed out that there is need for complete review and preparation of a comprehensive plan with a view to -bring the network to standards laid down by W.M.O.  The net work should come  into operation within 5 years. Similar action is necessary in respect of gauges maintained by the Irrigation Department of the States,

(Paras 2.26 & 2.27)

14. There are wide gaps in the hydrological data. No regular information has been maintained about the behaviour of the rivers. The river beds of some of the rivers are reported to have gone up due to reduced velocity of the flood and consequent accumulation of sand. This needs to be verified in the field.

(Para 2.28)

15. The Rashtriya Barh Ayog has referred to the new technologies    developed for collection,    transmission, storage and retrieval of basic data.  While we may not be able to modernise completely collection, transmission, processing and storage of data, a minimum programme should be taken up for meeting the essential requirement of flood forecasting.

(Para 2.29)

16. The present restriction on use of margin money on disaster preparedness measures should be reviewed. Funds need to be provided.

(Para 2.34)

17. The Committee  has already    recommended  a sub-plan approach for allocation of plan funds in respect of the backward areas. It has also dealth with extensively about the allocation of financial resources etc. The Sub-Plan approach would equally be applicable to the chronically flood affected areas identified by the States in accordance with the criteria recommended by the committee. The Committee has recommended a special grant of Rs. 5 lakhs per block, on a phased basis, to take care of certain special items like surveys, investigation etc. As in the case of chronically flood affected areas, a block would not be the unit for identification, but a basin or a sub-basin; the allocation may be on an area basis. A suitable formula would have to be devised so that this additional allocation is also available in respect of the chronically flood affected areas.

(Para 2.36)

# III. CROPPING STRATEGY

18. Adequate research support needs to be provided to solve 'Diara' land problems. Suitable research projects  should be  taken up on crop and varietal improvement,    efficient    methods of village for timely operations, efficient use of irrigation water, pests and disease management etc. Organised marketing system to pick up the farm produce from the producers and fetch remunerative prices will go a long way to promote this cropping strategy.

(Para 3.4)

19. Given such    facilities,    and    subject to local requirements, the general    cropping   pattern for the chronically flood prone areas of U.P. should be (a) intensive  'Rabi'    cropping  after    recession  of flood water with irrigation and raising crops with improved varieties of wheat, potato, peas and mustard; (b) after 'Rabi' irrigated summer cropping (Zaid) be practised, using suitable  short    duration    varieties of summer maize, mung or paddy  so  as to harvest the crops before rains;  and  (c)  'Kharif cropping when taken up, mostly flood tolerant paddy varieties like Madhu-kar, Chakia — 59 etc., may be adopted.

(Para 3.5)

20. The 'Diara' land in Bihar constitutes the most flood affected areas of the State. Diara lands of Bihar are  similar  in character to those  for eastern  Uttar Pradesh. The various practices in the 'Diara' land can be applied to other chronically flood affected areas wherever suitable.

(Para 3.6 & 3.7)

21. Access to irrigation water is essential for promoting intensive crop production    programmes    during flood free months in chronically flood prone areas of Bihar.   Adequate research support as advocated for 'Diara' lands in Uttar Pradesh holds good for Bihar.

(Para 3.7)

22. Flood incidence has been observed to be worst near the confluence of rivers in Assam. These areas which  are  chronically  flood  prone may continue to lack adequate flood protection for long years to come. Hence there is an urgent need for restructuring the cropping programme to minimise crop damage  and loss of production.

(Para 3.8)

23. In Assam Valley worst floods are experienced in the months of July and August, although in some years floods have been reported in early June or in end of September. In general, however, the cropping has to be restructured to avoid the months of July and August.

(Para 3.9)

24.  Recognising the flooding, pattern occurring in the riverine areas, the appropriate cropping strategy would be to raise early 'Ahu' paddy from February to June, followed by late transplanted  'Sali'  paddy from   September  to   December.   However,     farmers' acceptance of this strategy hinges on the availability of irrigation water for early planting of Ahu and for saving the 'Sali' paddy from moisture stress in the valley for year round surface flow irrigation due to topography, the ground water resources appear to be abundant.  It is indeed,  reported, that in most parts of the valley, ground water is available within a few metres of the surface and offers great scope for exploitation at fairly low cost.  The Committee advocates that steps should be taken to popularise an irrigated cropping programme of early 'Ahu' paddy or jute, in the pre-flood season, followed by late 'Sali' paddy or 'Rabi' wheat, mustard or pulses in the post-flood season. The State's efforts in the direction needs to be intensified using available high yielding varieties and technology.

(Para 3.11)

25. In the low lying deep water    areas,    farmers raise, crop mixtures of 'Ahu' and 'Bao' paddy. For 'Bao' paddy varieties like 'Kekola Bao', 'Negheri Bao' etc. are recommended, Nevertheless, the modern technology of paddy cultivation has not yet benefited the deep  water  paddy  culture  and there  is  no  breakthrough  yet in  deep water paddy  cultivation.  More intensive research has to be undertaken on deep water paddy.

(Para 3.12)

26. An  alternate  pathway  to   improve  production from  such  land  would warrant  systematic  development of deeper areas as organised water bodies for ,aquculture  and  use   the  same  as a  supplementary irrigation  source  for intensifying crop production in the remaining peripheral areas when properly drained. Recognising its merit,    the    committee    considers it would be worth-while to test the economic viability of this concept by undertaking a few operational pilot projects in the State before its large scale adoption.

(Para 3.13)

27. The Committee endorses the contigent crop plans and    alternate    cropping   pattern    envisaged by the Government of West Bengal.

(Para 3.15)

28. In general, agriculture in Orissa, means raising of paddy. The October-January sown crop of paddy, though covers only upto 5 per cent of the  State's paddy area, is practically free from flood and performs  best.     The season is comparatively cloudless and favours increased photo-synthetic efficiency from November  onwards.  All  efforts should  be made to expand paddy area in the October-January    season. The Committee advocates this  strategy in the flood prone coastal area of Orissa,

(Para 3.18)

29. The success of such a strategy depends on the availability of irrigation water. The Committee, therefore, reiterates its recommendations that immediate steps should be taken to increase irrigation facilities in the flood prone areas.

(Para 3.19)

30. Intensive research, carried out in the country by the scientists of the Central Rice Research Institute, Cuttack, Agricultural Universities etc. and elsewhere on paddy, now offers newer varieties and technology suitable for flood prone areas.   Photosensitive high yielding    varieties like CR — 1009,    CR— 1011, CR — 1018, Pankaj  and Jagnath can successfully be grown in rainfed, shallow and intermediate    waterlogged areas (15-50 cm water depth). For recurrent flood areas, flood    resistant    varieties like    FRG-7, FRG-8, BR-J3, BR-14, FR-13A and    FR-43B    are recommended.   Where  semi-deep   (50-100  cm)   flood water  conditions are  experienced,   rice  varieties  like CR-1030,  CR-260-30,  CR-260-31  etc.  would be  the suitable varieties. Floating rice varieties like Jaisuria, CNDW 332,    327, 326 and  325 have    shown great ecological adaptability and are recommended for deep water areas.

(Para 3.20)

31. The Committee advocates the restructuring of the cropping, which can escape or tolerate flood damage in the flood prone areas. For popularising such a cropping strategy, it is reiterated that steps should be taken to make available irrigation facilities in such areas.

(Para 3.21)

32. Due to management   difficulties,    deep   water paddy produces low grain yields, ranging from 0.5 to 1 ton per hectare. Suitable varieties are to be evolved to tolerate long periods of complete submergence. Nevertheless there appears no breakthrough in deep water paddy cultivation. In view of the importance of deep water paddy, in the flood prone areas and the formidable problems  faced for attaining any breakthrough in its production, the Committee strongly advocates intensification of scientific research on deep water paddy on priority basis.

(Para 3.22)

# IV. IRRIGATION STRATEGY

33. A strategy to retain some water in the natural depressions   for  providing  lift irrigation  during  the later part of the rabi season and during hot weather season should be considered.

(Para 4.6)

34. It should be possible to carry canal water for irrigating lands rendered flood-free during Rabi and summer seasons if there is any major,    medium or minor surface irrigation scheme operating in the relatively higher  areas  in the neighbourhood.  The distribution arrangements can be made from the nearest canal water course either through portable pipes or through underground pipe system which may remain undisturbed   during   the   floods.   Such  irrigation  will provide gravity flow to the areas rendered free from .floods for Rabi and hot weather crops in and around natural depressions. Drip irrigation and sprinkler irrigation may be tried to secure economy in water iise.

(Para 4.6)

35. Wells could be sunk in the areas.   They would be normally covered during the period of submergence and can be used for irrigation purposes with manual or animal operated devices as well as with portable pump sets to lift water from the wells in the floodfree season after the monsoon.

(Para 4.7)

36. In West Bengal many channels keep on flowing after the monsoon season  even after the lands are rendered flood free. To raise boro paddy or wheat the farmers are used to put up kucha bunds across the flowing channels to impound water and lift the same for irrigating the areas. The system is very crude and adversely affects the regimes of the natural streams or the drainage channels. Instead of putting up tern-  , porary earthen bunds, if a systematic programme of construction of sluices with gates are drawn up and construction undertaken, perhaps the purpose will be better achieved and during the monsoon season the gates can be kept opened to allow flood water to pass freely.

(Para 4.8)

37. A system of lifting water during the Rabi and summer  season  is  already  in  vogue  in  some  parts of the Assam State. This programme should be accelerated.

(Para 4.9)

38. So far as areas subjected to flash floods are concerned, the same strategy of tube wells, wells and river  lifts  can  be  considered  with  similar  portable arrangements for pumps, motors and distribution system   for  providing irrigation  during  Rabi  and  hot-weather seasons.  In such areas it is most advisable not to try any crops during flood periods,

(Para 4.12)

# V. MEASURES TO MITIGATE FLOOD DAMAGES

39. It is fully realised that absolute immunity from flood damage is not physically possible even in the distant future  because of unpredictability of several natural  forces which  might cause an unprecedented situation.

(Para 5.1)

40. The full potential of the Landsat Imagery be utilised to know precise details about the behaviour of various upper reaches in the country.

(Para 5.8)

41. The moderation of run-off would directly help the chronically flood affected areas. For reduction of run-off, the committee would recommend    (i) prohibition of production in the hilly catchments; (ii) cons-tructon  of flood  detention  reservoirs;   (iii)     contour bunding in hilly catchments; (iv) small check dams on the tributaries to delay run-off to point of concentration;   and (v) elaborate   arrangement   for   flood fighting arrangements at vulnerable points with adequate support of flood forecasting and warning thereof.

(Para 5.11)

42. A number of smaller flood retention reservoirs of suitable capacity should be constructed on or near each river, by excavation if necessary. This will serve to regulate the ferocity of flash floods down-stream of these reservoirs. The retained flood waters in various reservoirs can provide ample water supply during the dry season.

(Para 5.13)

43. The  upper reaches management  can  be most effective on a watershed management basis. However, at times a judicious choice between conflicting alternatives has to be made.

(Para 5.14)

44. Any individualistic attemps at soil conservation measures may not yield the    effective   results.    The whole watershed    needs    tackling in totality by. the Governments and  the individual fanners  should  be made to work within the prescribed norms. In consonance with the overall objectives, any financial needs of the   individual     farmers   should   be   satisfactorily backed by governmental agencies.

(Para 5.15)

45. Embankment construction has been one of the age old method of reducing flooding. The Committee agree  that  the   object  of remedial  measures of the protection of a chronically flood affected area should be  to  train the rivers  on  their way to the  sea by constructing protective  embankments, judicious dredging, flood escapes etc. One of the main reasons attributed to such frequent breaches has been found to be inadequate   maintenance.    The   Committee   endorses the Seventh Finance Commission recommendations on the subject.

(Para 5.17)

46. The importance of preparing a comprehensive plan of action assumes greater strength in the context of drainage management. The Committee would like  to emphasise involvement of all the concerned authorities /agencies which would  be responsible  for sanctioned construction works in the flood plain areas.

(Para 5.18)

47. The maintenance of drainage by dredging and utilisation of the material thus dredged for filling up the hollow areas on the other side of the embankments is a possibility.  The maintenance of major/medium drainages wherever maintained by Revenue Department, must be taken over by the Irrigation Department.

(Para 5.19)

48. The Committee, while endorsing the comprehensive treatment of the subject of drainages by the Rashtriya Barh Ayog would like to re-emphasis and recommend the following measures:

(i) There is need for closer coordination amongst concerned agencies like the Railways, National Highways, State Irrigation/Flood Control Departments so as to ensure that structures like bridges, roads, railways etc. do   not aggravate flood problems.

(ii) Prior     consultation by     National     Highway authorities.  State P.W.D.s and Railways with the State    Irrigation /Flood    Control    Departments should be made obligatory.    To facilitate an expeditious check, the Government of India   should   evolve   guidelines /checklist   for the   purpose of   vetting of waterways by the State Irrigation /Flood Control Departments,

(iii) It should be mandatory that assessment of adequacy of existing waterways should be made by the State Committee of Engineers or some other Technical Board and the waterways for bridges to be constructed in the future should be vetted by the State Irrigation /Flood Control Department.

(iv) The   Standing  Committee  for settling  disputes on waterways and sharing of costs, headed by the   Chairman,    Central    Water    Commission, should   be   vested   with   statutory   powers   for implementation  of  its decisions,

(v) The State should undertake legislation to prevent unauthorised river bed cultivation and encroachments into drains etc. and where such laws already exist, the   enforcement  agencies should   be   strengthened.   Cultivation of crops like water-melons, vegetables, etc. in river beds and  berms,  may     however,  be  allowed  with caution.    The    practice of cultivation in the abandoned beds of Dhars and which discharge into main rivers should be stopped.

(vi) Where suitable legislation with a penal clause for unauthorised crossings over drains has not been enacted, the same should be done and enforced.

(Para 5.20)

49. Flood relief channels should be constructed at suitable points to drain excess of flood water to remote artificial  lakes;  these  should also be provided towards the  downstreams and of enlarged channels to carry away surplus water to other artificial lakes. The flood relief channels can be used as feeders for minor irrigation canals. 				(Para 5.20)

50. A   complete   review   of   the   operation   of  the systems of sluices for drawing up a necessary operational manual for the same is necessary.

(Para 5.23)

51. The  paucity of data on river bed behaviours inhibits in making any objective idea about the problem of sand casting.  Studies should be undertaken whereby assessment of the problem in the right perspective can be had.

(Para 5.25)

52. The problem of sand casting, beyond a limit, is quite harmful for the crop growth. The Committee would recommend the initiation of scientific studies on the subject so that suitable crop planning can be devised. (Para 5.26)

53. Rural houses, facing flood fury, are generally made of  materials  which  cannot withstand  a  high degree of stresses and strains.   In the event of raising pucca structures the damage susceptibility can  be considerably reduced. Such a scheme should be supported in areas where alternatives are not found to be feasible. In case of its adoption strict enforcement would be desirable as otherwise additional numbers in the hope of receiving doles for contruction may get settled in affected areas.

(Para 5.29)

54. Raising of villages as a whole offers    another alternative to mitigate the hardships of human settlements. Without liberal support from public funds the proposition can rarely succeed. In case of raising of villages, roads should not be raised correspondingly so as to avoid any interference with drainage aspects. The roads may be allowed to get submerged during floods. Availability of country boats in sufficient numbers  would  be  able  to  solve  the  problems of the chronically flood affected areas during that spell.

(Para 5.31)

55. Construction of ring bunds around the villages or human settlements in another way which has been experimented at certain places.    Such a scheme may be  supported  in the event of cost-benefit  favouring the same in comparison to other alternatives.

(Para 5.32)

56. Structural changes and land elevation wherever undertaken by individuals or groups, should be encouraged and suitable monetary and other assistance be provided keeping in view the overall policy objectives.

(Para 5.33)

57. Strict regulation of land use in the chronically .flood affected areas is necessary.

(Para 534)

58. The Planning Commission already provided for soil  conservation  and  afforestation  measures  in  the upper catchment of flood prone rivers. This programme will require to be implemented on sub-watershed basins  after  identifying  the  critically  affected  ones. Effective implementation of this programme will require building of inter-disciplinary teams for each of the basins. The pace of the programme will have to be accelerated along with effective measures to prevent deterioration of new areas. The Committee would recommend special efforts in this direction.

(Para 5.34)

59. Disaster relief, while warding off, the immediate distress, encourages certain attitudes which need to be deplored. There is a tendency to consider relief measures as a right. This in turn tends to remove the incentive to avoid future flood losses and    encourages persistent human occupancy of the flood plain.

(Para 5.35)

60. Effective  steps should  be  taken  to  train and organise local volunteers in fighting flood hazards due to  threatened breaches in embankments and also to utilise  effective steps to  plug  the  breaches  as  and when the same occur.

(Para 5.36)

61. The Committee feels that there should be a law to ensure that any building that is constructed in such areas should provide for a plinth above the normal flood level.

(Para 5.37)

# 1. INTRODUCTION

1.1 Floods constitute one of the most serious environmental hazards and the problems of flood control, and the measures to be taken for relieving the distress  of  the  flood  affected  population  have  been engaging the attention of Government and the planners   for  a  considerable length   of  time.  There  are, nevertheless,  substantial    areas    which    suffer from heavy floods at frequent intervals resulting in serious crop losses, damage to houses, roads and other physical  infrastructure, institutional  properties,  and  dislocation of normal economic activity in the area from time to time. The economic growth of such areas has been and continuance to be impeded generally clue to frequency of heavy floods, and special measures are, therefore, necessary for    promoting their    economic development. The    National Committee has accordingly decided that chronically flood affected areas  should also be treated thereafter as backward areas, and special measures instituted for dealing with their problems, and promoting their economic development.

1.2 The Rashtriya Barh Ayog (1980) has examined at considerable length the various factors that cause heavy floods in different river basins and deltas, and indicated the measures that need be taken for affording such flood protection as may be feasible in such areas. They have in particular recommended the measures to be taken for moderating the intensity of floods and reducing flood damage. The Rashtriya Barh Ayog has  listed  five  States  which  need  urgent  help and attention for the purpose of flood control. These are Assam,  Bihar,   Orissa,   Uttar  Pradesh     and     West Bengal.

1.3 In Assam, there are two distinct physiographi-cal regions viz., the Bramaputra Valley and the Barak Valley. The major problems that we are confronted with in the Bramaputra Valley are: —

(i) over bank spilling from the Bramaputra and its major tributaries;

(ii) drainage congestion; and (iii) erosion and silting in various areas.

In Barak Valley, the main problem  is inundation from river spills and drainage congestion.

1.4 In   Bihar,  floods   occur  frequently  over  large areas in North Bihar, and also along the flood plains of the Ganga at Places in South Bihar. The main contributory factors are:

(i) spillage in the snow fed rivers in North Bihar coming from the mountaineous regions; and

(ii) heavy silting and tendency of some  of these rivers to frequent breaches and avulsions.

There is also blockage in the tributaries of Ganga on both the north bank and south    bank when the Ganga itself is in high floods, besides drainage congestion in depressions and low-lying flood areas.

1.5 In Orissa, floods, occur mainly in the deltas o the  more  important  rivers   viz.,  the Mahanadi,  the Baitarni, the Brahmani and- the Subarnarekha. Som« of the  existing test relief    embankments which an rather low and were constructed without due regarc to engineering specifications often breach, and cause heavy  damage.  Bank erosion and  sand casting also arise in some areas from time to time.

1.6 In Uttar Pradesh, major floods are caused by various over spillage in rivers like the  Ghagra, the Rapti and .the Gandak coming from high mountainous regions of Nepal.    There are also high floods in the Ganga and Yamuna from time to time.

1.7 In West Bengal, heavy floods have been caused in  recent  years  in  the  Mahananda  basin  in  North Bengal through over-spillage of the banks, breach in embankments, and change in the course of some channels. In Central Bengal, also serious floods have occurred  in recent years due to the  over-spillage of the Mahananda and,    more or less,    simultaneous high floods in Ganga. In the South Bengal region, heavy floods have occurred in recent years due to drainage congestion on account of deterioration in the regime of main rivers like the Saraswati, the Damodar, the Kana   Damodar, the  Kana  Nadi,   Roopnarayan,  the Dwarakeshwar, the Silabati and Kargsabati. The situation is aggravated during periods when there is also blockage   of   inland  drainage  due   to   sea  tides and cyclonic storms.

1.8 Traditionally, where the arable lands are liable to floods, people have tried to protect themselves from the inundation and possible damage by building embankments to keep off the flood waters. Construction of embankment has been going on in the river basins for centuries. Many states have passed legislation to control the intrusions and obstructions in the flood plains so as to maintain the drainage  system most effectively and prevent blocking the flood to the detriment of the general population. After, freedom, many of these legislative controls appear to have been overlooked  and  embankment  construction  has  generally been in haphazard manner.

1.9 Because of the haphazard construction of embankments and non-maintenance of key embankments the  experience has  been a  continuous breaching of embankments  which  were  supposed  to  protect large areas.    Thanks to these breaches, the damage in the 'protected' areas is much more substantial than what it could have been had the areas not been protected.

1.10 The National Committee has carefully considered the objective criterion to be laid down for the demarcation of chronically flood affected areas. The franchise  of the  Committee  is not  only to  identify the areas of backwardness but also to suggest remedies for improving the productivity and economics of these backward  areas.  Embankment  breaches  and   consequent damages are, in most cases, man-made. By and large, the remedy has to be sought only in people disciplining themselves to ensure that technical advice in these matters is obeyed meticulously and legislative controls    imposed by the    legislatures are faithfully observed.

1.11 The National Committee has, therefore, decided that it should not address itself to areas v/here damages are caused by human action referred to in para 1.10. It is confining itself only to the ameliorating steps necessary  for the  development of the affected areas where damage is caused by natural havoc and is in  the flood  plains v/here neither any embankment exists nor are provided in the Master Plan. This is where nature's direct havoc on the economy is felt. Again it is this havoc, which, if chronic, creates the problem of backwardness. The aim of the Committee, therefore, is to deal with such unprotected areas where natural havoc is chronic and    suggest    ameliorating measures.

1.12 Although a number of Committees and Commissions have been appointed to deal with the flood control measures, no proper attempt has so far been made to identify the areas which are unprotected from chronic havoc and to consider steps for ameliorating tfoe problems in those areas. The National Committee has, therefore, decided to  submit a separate report about the developmental problems and the approach in these areas as their problem and remedies have to be highly location specific and different from the normal developmental programmes.

1.13 At the outset, the Committee would hasten to add that it has greatly been handicapped by lack of basic data. The Committee is,    however, grateful to the State Governments particularly West Bengal, Uttar Pradesh,   Orissa  and   Bihar,   which     extended   their whole-hearted   support   in   giving  whatever  information was available with them. The Committee would particularly like to thank Shri S. K. Banerji, formerly Adviser, Planning Commission and now Member of the State Planning Board in Bihar, who was also one time Chairman of the Ganges Flood Commission for giving valuable    assistance to the Committee in drafting its report.   The Committee has also benefited by the advice of several experts in the field particularly those in Central Water Commission, Ministry of Agriculture etc.

1.14 In the following chapters, the Committee has attempted to deal with the criteria for identification of chronically flood affected areas, strategy of development   and   suggested   specific  lines   of  action  for development  of     cropping  patterns  and     irrigation which, by far, are the most important requirement for the development in    these areas and also deal with the steps necessary for mitigating the flood damage and providing shelter to the human settlements.

# 2. IDENTIFICATION OF CHRONICALLY FLOOD AFFECTED AREAS AND STRATEGY TOWARDS DEVELOPMENT

At the outset, the National Committee would like to define the objective criteria for the demarcation of the chronically flood affected areas.

2.2 Within the flood    plains, not all areas where the flood reaches at any    time are really damaged. Damage is of two kinds:   (i) crop damage; and (ii) damage  to houses,  cattle,     infrastructure and other property. Crop damage can occur if the crop selected by the farmer is susceptible to water logging. People have adjusted themselves to the nature of the environment in areas which are flooded, by mainly growing paddy in these areas. 'By sheer experience they have also evolved methods to grow the right type of paddy which normally would escape flood damage by complete submersion. The paddy plant can survive even if the flood flows over the crop for 7 days at a stretch. Only where  the     current is strong and uproots the plants, real damage can occur where the flood is less than 7 days. These areas are marginal. House and cattle-damage can occur where the habitations are low and the force of the current erodes foundations and where habitations have been located in areas where flood flows can be at high   speed. Owing to lack of habitable areas and the pressure of population many spots unsuitable in the    flood plain have been made into human habitations. This will be in areas which are generally flooded to some depth chronically. Normally it will be found that areas that may be flooded to cause crop damage of a severe nature to the paddy cultivation will also be the areas where house damage and cattle .damage occur.  The Committee, therefore, is of the view that if the problem of crop damage and the area involved is identified, the other    problem areas will automatically be identified to a large extent.

2.3 Living in the flood plains the householder must be insuring himself against periodic floods.  Only if the frequency of floods is more than tolerable, he is at a disadvantage.  The Committee, therefore, considers that a chronically flood affected area should be defined as one where the flood frequency is at least once in three years. At the same time, not all these areas will be liable .to crop or house damage unless the level of the water in that area leads to crop damage and the force of the water leads to house damage.

2.4 The  above     criteria of once in    three years flooding  would     have  to be further refined  taking into account the  flood duration at a stretch,  flood depth,  flash  floods,  etc.  The  Committee  would  recommend the following criteria for identification of the chronically flood prone areas: —

(i) flood     frequency  of  at least  once  in  three years,

(ii) flood .duration of at least 7 days period at a stretch.

(iii) flood depth of more than the standing paddy at that time, and

(iv) flash floods with strong current liable to uproot plants even if the duration is less than 7 days.

2.5 The  Committee is cognisant of the fact that the above exercise, can be undertaken only if certain basic data is available. The Rashtriya Barh Ayog tried to collect figures of the flood fluctuation within a year in various flood plains but the relevant data was not. available. The Committee would strongly recommend that in all flood plains, one single Department must be designated as  the  Department to maintain  sufficient hydraulic data. It is only this data which wculd enable a demarcation of the chronic flood aflecled areas and the nature and the change in such areas over time.

2.6 The Committee tried to get some data, on the above approach, from the Ganga Commission and the States about some blocks, which, are impressionistical-   . ly considered to be chronic flood affected blocks. It has not been possible to get much information from existing records on this subject. As a result, some de» tailed work was done on the Kandi block in West Bengal which is supposed to b& a chronically flood affected block and the result of the investigations are as under: —

| Kandi Block |
| --- |
| Year | Extent of flooding (acres) | Duration of flooding (days) | Population affected | Cropped area damaged (acres) | No. of houses damaged |
| 1 | 2 | 3 | 4 | 5 | 6 |
| 1977 | 24,900 | 3 | 60;OOQ | 18,000 | 285 |
| 1978 | 50,000 | 20 | 1,10,000 | 33,000 | 16,000 |
| 1979 | Nil |
| 1980 | 5,800 | 5 | 10,000 | 4,400 | 230 |

During  1978 the    flood level was above R.L.  53.8 (maximum R.L. 57.3) for 12 days, above R.L. 48.8 for 20 days and above R.L. 46.3 for 84 days.   During 1977 the flood level was above R.L. 48.8 for 6 days and above R.L. 46.3 for 23 days; statistics of 1978 reveal that the flood level was   above R.L. 46.3 for 8 days.

2.7 The above shows that the area affected in three of the years was by a flood duration of less than 7 days. Crop damage, if any, could not have been severe unless the wrong crop had been selected or it was in the river Sow. These data are not available.    In only one year the duration of the flood lasted for 20 days  but here  again there is no distinction of  the area  which   should normally  have  had  damage   because of water stagnation beyond 7 days. This .block turns out to be a chronic flood affected block on the criterion of flood patterns in these three years. The area  that will have  to  receive     ameliorative  action may be found to be reasonably small. The Committee wants to emphasise that a general cry of flood damage and non-Identification of the reasons for the damage and the area actually damaged will only lead to wrong methods for amelioration.

2.8 Steps  will have  to  be taken to identify  sue! areas before ameliorative action can really be started. The Committee recommends that in all the blocks affected by floods, this exercise to refine the identification of chronic flood affected areas requiring amelioration may be done within the next two years so that  a   realistic   and     satisfactory   ameliorative   programme can be introduced. What is. required is preparation of a    relief map of the area in the village plan  annually   giving   the  various   contours   affected by  flood waters  during  the  period  demarcating  the areas which were     flooded more than 7 days at a stretch  and  within these   areas  where the  depth  of water  was  for  7 days at a  stretch higher than  the level of the traditional paddy crop grown in the area. Thus, the relief maps will have to give three contours for  each season.   We  recommend  that  this  exercise should now be done for every »year so that the nation gets  a correct idea  of what area are susceptible to damage in present circumstances and needs out attention. The fact that 40 million hectares are liable to floods in a year is of no relevance for the problem of development of areas which are chronic flood affected. The Committee has no hesitation in saying that the actual area requiring attention will be much smaller than   the  actual  area  liable  to  flood.     Ameliorative measures can be purposeful and relevant 'to the problem   only when  the^ demarcation  of  such  areas   is technically correct  and  sound. Annexure  2.1  reveals the  extent   of   flood  damages   in  the  country   as   a whole. The main point of interest here is that crop area   damaged is     much   less  than   the  total  flood affected  area.   The     chronically   flood   affected   area would     naturally be  much less than the crop area damaged   because  the   latter  includes   crop   damage due to enbankrnent breaches.    Annexures 2.2 to 2,4 indicate  the  frequency  and extent of flooding  data obtained  from  the  States  of  Orissa. Uttar Pradesh and West Bengal.

2.9 Unlike the demarcation area of a block which the Committee has deemed useful for planning in its reports   already   submitted,   the  area  considered  appropriate for the present report, for obvious reasons, is a water basin or sub-basin.

2.10 Heavy floods thoroughly upset the    economy of chronically flood affected areas. Year after year, our country suffers from incalculable losses of human life, property, livestock and farm produce. Flood plain occupancy depicts an inherent major dilerna.  Whilst providing attractive locations for various human activities on account of the rich alluvial soils, the flood plain occupancy can prove very costly and disastrous in times of chronic floods and may exact a heavy toll of property damage, income loss of life as well.    In-spite of these hazards caused, there has been no halt to the new settlements in the flood plains and rather mushrooming of settlements in the hitherto uninhabited area is often seen. The growing pressure of population on land and its contribution to enlarging the extent of damage has been compounded by the growing spread and intensity of floods    themselves. The latter, in turn, has been the result of several factors, the most important of them being the deterioration of river  channels.  Their beds  raised by  increasing  silt deposition, they are unable to carry the heavy monsoon flow which spills over their banks.

2.11 There has been an increasing awareness that absolute control and protection against floods can be seldom achieved. Complete protection against floods, though technically feasible, may not be economically justifiable or possible.   Each flood control measure, be it a dike or flood wail or reservoir, has a limited effectiveness.

2.12 A changing perspective on flood loss prevention and management is a prerequisite for dealing with chronic flood affected areas.  Attention has, of late been focused on several aspects; there are, however quite a few more which need urgent or added attention. The problem needs priority attention, and has to be dealt with on a continuous basis rather than ad-hoc, and    must be    viewed in 'a    comprehensive fashion.   Traditional crisis — provoked approach deserves to be replaced by flood management approach and needs to be seen as a part and parcel of the social and economic developmental plans. In general the interest in floods has been following a pattern of short busts of feverish activity following a flood event, and the normal action had been to clear up the debris and ease   the sufferings of the victims, followed up by setting up of enquiry committee and then the whole affair folding up with passage of time.

2.13    For reducing the flood damages effectively a number of measures are possible.    No single measure may provide the right answer and as such adoption of a combination of measures becomes desirable.   Tampering with nature on a macro scale is always fraught with risk and care must be taken not to disturb   the natural regime of rivers.    The mounting magnitude of flood damage is a pointer to the fact that either the measures adopted   thus far had been out of tune or rather insufficient or incommensurate with the needs. This necessitates a fresh   look- for a deeper probe at the problem.

2. 14   The Committee considers that the development of the chronic flood affected areas has to be looked at as a whole and the approach would require a comprehensive and integrated development. While modification of floods, reduction in damage susceptibilities of    infrastructure    and property    etc.    are no doubt important components of an integrated approach, the development problems has also to take into account the steps necessary for exploitation of the potential available and the    problems of human    settlements. The engineering    and other    aspects of flooding like content of upper reaches control, embankments, maintenance, drainage control, control    of sanding /silting, sand casting etc. are, by and large, engineering problems and have been dealt with at length, in the Rashtriya Barh Ayog report. We in this Chapter are trying to deal with the developmental problems and touch upon, the engineering    problems like    embankments to the extent they affected the development problems.

2.15    The Committee considers that the measures to mitigate    flood    losses need to be part of a comprehensive scheme wherein modifications of floods, reduced damage susceptibilities of infrastructure and property  are looked at in an integrated fashion. These have been viewed so far in the content of upper reaches control, embankment, maintenance, drainage management and control    of sanding /silting, alongwith    Fhe measures  to deal with  sand casting.    The  problems of human    settlements    would also deserve    rightful attention.    The engineering and other aspects of flooding   as   already noted have been dealt with at length in the report of the Rashtriya Barh Ayog.   The relevant recommendations of the   Rashtriya Barh   Ayog   have broadly been endorsed and wherever necessary modifications and  additional recommendations    have  been highlighted in a separate Chapter.

2.16    Before    undertaking any development profile for the area identified as chronically flood affected   in accordance with the criteria indicated by us earlier   in this Chapter, it would be   necessary to draw a Master Plan based on proper surveys and investigations for the basin and sub-basin   affected.    The Committee has recommended earlier the concept of an Integrated Project Development Authority in its report on "Organisation of Administrative and Financial Structures for Backward   Area   Development".    The     Committee would suggest that in the case of chronically flood affected areas; the project approach should be based on a basin or sub-basin approach.  It is quite likely that some of the sub-basins or basins may not cover the whole block and only a part of the block may be covered. The Committee feels that for developmental purposes it should not be difficult for a project approach to be implemented covering part area of the blocks so long as they fall within a basin or sub-basin.    Detailed surveys and preparation of contour maps for the development of the areas identified require first priority.    Such maps would help not only for formulating of developmental-plans but also in forecasting more accurately the areas likely to be affected by floods   thereby avoiding unnecessary evacuation from areas not likely to be affected.

2.17    The   Committee has already pointed out that most of the chronically flood affected areas lie in the five States of Uttar Pradesh, Bihar, Assam, West Bengal and Orissa.    The crop    damage is one of the worst damages    caused in     floods,   For    instance, during 1976-78 block years, the crop area affected by floods aggregates on an averge to 41.05 lakh hectares annually for these States. Such magnitude of flood damage to cropped area in these areas keep the conditions of local farmers backward and unstable. An appropriate cropping strategy and other steps have therefore to be adopted in these areas.   The obvious pathways would be to popularise suitable flood escaping or flood tolerant cropping system or intensive crop production with irrigation in the flood free months there. The Committee considers that maximum utilisation of the water resources available in these areas and introduction of suitable cropping strategies would be the most important steps for the development of these areas. These are dealt with in greater detail in relevant chapters.

2.18   The next in importance is the damage caused to houses, property and infrastructure.   The, chronically flood affected areas are often densely populated. Flood extract a heavy toll year after year in respect of damaged and swept away houses. According to the information collected by the Rashtriya Barh Ayog, on an average, 9.25 lakh houses were damaged each year during    the last 25    years.    Quite a few alternatives have been considered for minimising the damage to the houses It will not be socially possible to shift large number of people to higher grounds.    Strengthening of house    structures,    raising the level of   whole villages or providing ring bunds around villages have been considered as  possible  alternatives.   Each    of these alternatives has positive and negative    aspects; yet the fact remains that something has got to be done to provide protection to the human settlement.    The Committee has dealt with this matter in all its aspects in a, separate Chapter.

2.19    The Committee would also like to emphasise the importance of pre-disaster preparedness measures since they can change a major disaster into a minor one and mitigate the suffering of those likely to    be affected.    Disaster preparedness involves a long chain action beginning with    forecasting,  issue  of  timely warning,    reaching the    warning to the persons concerned  in time,    advance    preparation of contingent plans in respect of precautionary measures for safety and    security of lives and   property, education    and training of the people in the vulnerable areas in various aspects relating to  prevention and protection, stockpiling of supplies,  organisational    arrangements for disaster    management  and  earmarking  of  necessary funds,

2.20   Timely issue of warning about the occurrence of floods and their nature and intensity is basic for disaster preparedness since it .will enable people    in the vulnerable areas to move to safer places with their moveable property where this is considered necessary or take adequate precautions where evacuation is not necessary.    Concentration of rainfall during the rainy season in a few spells of heavy rain is the direct cause of floods.    Most of the floods occur during the monsoon and are also assoicated with tropical storms and depressions. Location and    monitoring    the progress of depression and storms, predicting their future behaviour, and supply or reliable rainfall data has been among the major tasks of the   Indian Meteorological Department.

2.21 Cloud pictures are transmitted twice a day by the polar orbiting Satellites and these are received by 7 automatic transmission receiving stations of the Meteorological  Department. These pictures do not, however, reveal the nature and strength of the depression and its other parameters.  The special Weather Satellite transmits very high resolution pictures. Special terminals are being set up by the I.M.D., N.R.S.A. and I.S.R.O. for receiving these pictures   I.M.D. is proposing to acquire some specialised aircraft to penetrate through the eye of the cyclones and make actual in-situ observation of wind, temperature and pressure between the cyclone-fields and provide the basis for ground truthing of the Satellite data. When the Gas-stationary Satellite starts transmitting data it will be possible to have observations once in two hours.

2.22    Radars which can detect and tract the course of the depressions and cyclones within a distance of 400 Kms. have been set up at"   Calcutta,    Paradeep, Vizag, Madras and    Karaikal in the East-coast and Calicut, Bombay and Goa in the West Coast.    One more Radar is being set up at Musulipatnam.    The Meteorological Department is also    maintaining 32 Observatories manned by Departmental staff and 31 manned by extra departmental employees along the coastal belt of India. These Observatories take 6 observations   a   day   about rainfall   and   wind at  fixed Departmental Observatories equipped with self-recording instruments.   In some inaccessible areas automatic recorders with radio communication equipments have been set up. The Meteorological Department also maintains 30 Pilot Balloon Observatories for taking upper wind observations, atmospheric pressure, temperature, humidity etc.  The weather data collected by the Meteorological Department is made available to the Central Flood Forecasting Organisation of the Central Water Commission.

2.23   There are many improvements that need to be carried out urgently   to improve the   efficiency of the Meteorological services.    These include: —

(i) Conversion of part-time observatories into full-time ones with self-recording instruments;

(ii) Conversion of selected Pilot    Balloon    Observatories   into Radio Wind   Stations;

(iii) Augmenting the   Radar Stations;

(iv) Provision of effective communication links between Radar Stations and    Meteorological Centres;

(v) Modernising the Radar stations and providing them with equipments to transmit the pictures to the concerned cyclone warning centres; and.

(vi) Expediting the    acquisition of air-crafts    for cyclone reconnaissance,

2.24   The  Meteorological  Department  is  reported to have drawn up a comprehensive scheme    for this and other    immediate    requirements for    improving meteorological telecommunication net-work for collection of data and its prompt dissemination to the appropriate quarters.    The Committee would suggest early decision to these proposals.

2.25   Rainfall data is crucial for flood forecasting. The Rashtriya    Barh    Ayog has reported that as on 31-3-1979 there were 1092 ordinary and 614b self-recording rain-gauge stations maintained by the Meteorological Department.   The State Governments and other organisations maintain 3791 ordinary rain-gauge stations.   The Rashtriya Barh Ayog has emphasised the need for designing self-recording rain-gauge network for flood   forecasting   with   a   view to   ensure adequate coverage of the catchment of the upper and lower reaches  of the important rivers.    The present position regarding maintenance of rain gauges by the agencies of State Governments, recording of rainfall, transmission of data etc., need to be streamlined.    The work is not always taken    seriously by staff who get only a very small honorarium for doing    this   work. Rainfall data   should   be scrutinised and   published since it is a valuable record. It is of utmost importance that the flood forecasting stations are enabled to get rainfall data relating to the catchment of the rivers as well as their lower reaches without delay during the flood season.

2.26 The Central Flood Forecasting Organisation is maintaining a net-work of observation stations where gauges have been installed to record river flows, sediment discharge etc.    The Rashtriya Barh Ayog have pointed out that there is need for   complete    review and preparation of a comprehensive plan with a view to bring the net-work to standards laid down by W.M.O. (World   Meteorological   Organisation).   The   net-work should come into operation within 5 years. This is very important recommendation and its implementation will improve flood forecasting.

2.27   Similar action is necessary in respect of gauges maintained by    the    Irrigation    Departments of the states.

2.28    There are wide gaps in the hydrological data. No regular information has been maintained about the behaviour of the rivers.    The river beds of some of the rivers are reported to have gone up due to reduced velocity of the flood and consequent accumulation of sand.    This needs to be verified in the field.    A study on the Mahanadi on para 5.24 of Chapter 5 shows how impression can be wrong.    Without basic hydrological data flood control works cannot be planned properly.

2.29 The Rashtriya Barh Ayog has referred to the new technologies developed for collection, transmissions, storage and retrieval of basic data.   These include use of automatic recording instruments — (like Radio Reporting Rain-gauge Instruments, automatic water level recorders etc.), Radar (for measurement of rainfall, stream velocity and soil moisture), aerial photography, remote sensing and use of computers. While we may not be able to modernise completely collection, transmissions, processing and storage of data, a minimum programme should be taken up for meeting the essential requirement of flood forecasting.

2.30   Government of India had introduced centrally sponsored schemes providing for 100 per cent grant for soil survey, topographical survey etc., under Command Area   Development   Programme.    It is essential   that surveys and data collection schemes relating to flood forecasting and flood   control are fully   financed by Government of India    and    their    progress    closely monitored.

2.31 Recent advances in forecasting techniques have made it possible   to provide   warning   sufficiently in advance excepting in rare cases of flash floods with unforeseen intensity.   Unless the warning reaches the concerned people in sufficient time, it may not serve its purpose.    Telephones    and    telegrams    usually    fail during the   monsoon    season.   The Posts and Telegraphs Department should have special arrangements to maintain these facilities during the flood season in the chronically flood affected areas.    Teleprinters network should be established to connect the Sub-Divisional and District    Headquarters in the chronically flood affected    areas.    The Taluk and Block Headquarters should be connected by phones.    Temporary phones should be provided to all persons concerned with disaster management.

2.32    Police    Wireless has been the most reliable source of communication during disaster.    Since it is essentially meant for communicating messages regarding law and    order, its capacity is    stretched to the utmost during disasters.   During monsoon, temporary wireless sets are established for meeting the   requirements of   Irrigation   Department as well as the relief administration.    The requirements in this regard are not fully met due to want of adequate number of sets and supporting arrangements.    The Wireless net-work should be equipped to shoulder the additional burden imposed by natural calamities.   A certain amount of modernisation is also necessary.    The extra expenditure on the expansion and improvement of wireless system should  come  from  resources earmarked for disaster preparedness and relief measures.    The normal police budget is not able to provide for this.

2.33  There is generally no  adequate   stock-piling of essential supplies and there is considerable time-lag in procuring these after the    occurrence of flood. Movement is also handicapped due to poor road communication facilities in the affected areas and transport arrangements.    Certain items like power and country boats, lifebuoys, tents, tarpaulins etc., have to be kept at vulnerable locations before they are cut off.

2.34    Disaster    preparedness    measures are not a charge on margin money provided to State Governments on the    recommendations of   the   Seventh    Finance Commission.   Margin money can be used only for rescue, relief and rehabilitation after the occurrence of the natural    calamity.   In   view of the resources constraint experienced by State Governments, they are not able to provide adequate funds for disaster preparedness measures outlined in the foregoing paragraphs.   Prevention is always better than cure.   Disaster preparedness can mitigate the effects of disaster and funds allotted for this purpose can result in considerable saving in the post-disaster period and hence on recurring expenditure or reserve relief .and rehabilitation. The present" restriction on use of margin money on disaster preparedness measures should be reviewed.   Funds need to be provided.

2.35 The Committee has emphasised the need for development of irrigation, crop production, protection to houses and property,    disaster    preparedness etc. This does not mean that the scope for other developmental activities in these areas does not exist. For instance, in certain areas of Bihar, keeping of buffaloes and undertaking fish culture in the stagnating water Is an important subsidiary occupation in these areas.   The proposed Project    Authority,    when it undertakes a complete survey, would naturally come to know about the potential possibilities.   Whatever be the potential, it would have to be developed.

2.36    The Committee has already recommended a Sub-Plan    approach for allocation of plan funds   in respect of the backward areas.   It has also dealt with extensively about the allocation of financial resources etc.    The Sub-Plan approach would equally be applicable to the chronically flood affected areas identified by the States in accordance with the criteria recommended by the Committee.   The Committee has recommended a   special   grant of Rs. 5 lakhs per   block, on a phased basis, to take care of certain special items like surveys, investigation etc.   As in the case of chronically flood affected   areas, a block would not be the unit for identification, but a basin or a sub-basin; the allocation may be on an area basis.   A suitable formula would have to be devised so that this additional allocation is also available in respect of the chronically flood affected areas.

| Annexure2.1 |
| --- |
| FLOOD DAMAGE DURING 1953 TO 1980 |
| S.No. | Year | Area Affected (lakhs) | Population affected (lakhs) | Darn age to crops. |
|  |  |  |  | Area (lakhs ha.) | Valu (Rs. lakhs) at current price |
| 1. | 1953 | 59. 4 | 252.8 | 9.3 | 4206.0 |
| 2. | 1954 | 74.8 | 182.4 | 26.5 | 4100.1 |
| 3. | 1955 | 111.7 | 309.5 | 54.0 | 7795.5 |
| 4. | 1956 | 80.1 | 148.4 | 21.0 | 4203.2 |
| 5. | 1957 | 49.7 | 77.9 | 4.5 | 1455.6 |
| 6. | 1958 | 62.4 | 114.4 | 14.9 | 4353.4 |
| 7. | 1959 | 42. 0 | 138.9 | 15.4 | 5721.7 |
| 8. | 1960 | 76.3 | 86.8 | 26.5 | 4613.2 |
| 9. | 1961 | 65.3 | 93.1 | 18.3 | 2494.5 |
| 10. | 1962 | 61.2 | 157.3 | 35.6 | 8028.7 |
| 11. | 1963 | 35.6 | 111.9 | 19.7 | 3123.6 |
| 12 | 1964 | 46.2 | 140.0 | 24.7 | 5708.3 |
| 13. | 1965 | 10.4 | 33.0 | 2.5 | 541.3 |
| 14 | 1966 | 42.3 | 124.1 | 16.1 | 6404.0 |
| 15. | 1967 | 70.8 | 265.0 | 33.0 | 11955.0 |
| 16. | 1968 | 82.5 | 214.7 | 26.9 | 13710.1 |
| 17. | 1969 | 95.4 | 320.0 | 43.4 | 21101.9 |
| 18. | 1970 | 84.5 | 322.4 | 48.5 | 16178.1 |
| 19. | 1971 | 132.5 | 596.5 | 62.4 | 42262.8 |
| 20. | 1972 | 57.2 | 271.6 | 24.4 | 9855.8 |
| 21. | 1973' | 137.2 | 635.9 | 76.0 | 42803.0 |
| 22. | 1974 . • | 67.0 | 294.4 | 33.0 | 41163.1 |
| 23. | 1975 | 61.5 | 313.5 | 38.5 | 27118.8 |
| 24. | 1976 | 178.9 | 505.2 | 76.8 | 59507.5 |
| 25. | 1977 | 174.3 | 495.4 | 82.6 | 72062.7 |
| 26. | 1978 | 186.1 | 704.5 | 99.6 | 91108.4 |
| 27. | 1979 | 39.8 | 195.2 | 21.7 | 76997.4 |
| 28. | 1980 | 114.2 | 540.9 | 55.5 | 36613.7 |
|  | Total | 2299.3 | 7644.8 | 1011.8 | 565887.1 |
|  | Maximum | 186.1 (1978) | 704.5 (1978) | 99. 6 (1978) | 91108.1 (1978) |
|  | Average | 82.1 | 273.0 | 36. 1 | 20185.3 |

| Annexure 2.1 |
| --- |
| FLOOD DAMAGE DURING 1953 TO 1980 |
| S.No. | Year | Damage to Nos. | houses Value (Rs.) | Cattle lost No. | Human lives lost No. | Damage to public utilities (Rs. lakhs) | Total damage to crop public utilities (Col'. 6 + 8 + 11) (Rs. lakhs) |
| 1 | 2 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1. | 1953 | 98838 | 924.0 | 57028 | 34 | 290.0 | 5420.0 |
| 2. | 1954 | 220060 | 672.1 | 22514 | 279 | 1015.7 | 5787.9 |
| 3. | 1955 | 1741978 | 3278.4 | 77437 | 889 | 795.6 | 11869.5 |
| 4. | 1956 | 721199 | 808.0 | 16903 | 462 | 121.6 | 5132.8 |
| 5. | 1957 | 314577 | 527.4 | 77537 | 304 | 419.7 | 2402.7 |
| 6. | 1958 | 461316 | 616.3 | 18766 | 400 | 179.2 | 51489 |
| 7. | 1959 | 652622 | 944.0 | 66479 | 622 | 1202.3 | 7868.0 |
| 8. | 1960 | 651720 | 1482.6 | 14982 | 520 | 648.4 | 6744.2 |
| 9. | 1961 | 817861 | 97.0 | 18061 | 1389 | 634.1 | 3225.6 |
| 10. | 1962 | 520741 | 1145.5 | 39814 | 354 | 105.1 | 9279.3 |
| 11. | 1963 | 406994 | 372.7 | 4915 | 419 | 312.0 | 3808.3 |
| 12. | 1964 | 266634 | 479.8 | 5430 | 695 | 536.4 | 6724-5 |
| 13. | 1965 | 32451 | 15.7 | 7294 | 68 | 4.2 | 561.2 |
| 14. | 1966 | 156601 | 77.0 | 8868 | 165 | 41.0 | 6522.0 |
| 15. | 1967 | 601316 | 984.0 | 5921 | 358 | 738.0 | 13677.0 |
| 16. | 1968 | 798661 | 4028.3 | 130356 | 3498 | 2533.3 | 20271.7 |
| 17. | 1969 | 1242287 | 5378.9 | 271073 | 1401 | 6850.6 | 3333.4 |
| 18. | 1970 | 1434029 | 4860.6 | 19198 | 1076 | 7643.3 | 28682.0 |
| 19. | 1971 | 2428044 | 8024.1 | 12866 | 1141 | 12911.3 | 63198.2 |
| 20. | 1972 | 897257 | 1246.0 | 58861 | 544 | 4717.4 | 15819.2 |
| 21. | 1973 | 869897 | 5257.2 | 261016 | 1349 | 8848.0 | 56908.2 |
| 22. | 1974 | 746709 | 7240.3 | 16846 | 393 | 8494.0 | 56897.4 |
| 23. | 1975 | 793704 | 3408.3 | 17345 | 685 | 16600.0 | 46127.4 |
| 24. | 1976 | 1745501 | 9215.9 | 80057 | 1374 | 20151.9 | 88875.3 |
| 25. | 1977 | 1666625 | 15228.8 | 556326 | 11316 | 32889.0 | 120190.5 |
| 26. | 1978 | 3507242 | 16757.4 | 239180 | 3396 | 37610.1 | 145475.6 |
| 27. | 1979 | 1328712 | 21060.6 | 618248 | 3637 | 23362.7 | 61420.7 |
| 28. | 1980 | 2530936 | 17085.1 | 59401 | 1903 | 29302.7 | 83001.5 |
| Total | 27600457 | 131216.3 | 2710822 | 38693 | 218072.5 | 9153759 |
| Maximum | 3507243 (1978) | 210606 (1979) | 618248 (1979) | 11316 (1977) | 37610.1 (1978) | 145475-6 (1978) |
| Average | 985731 | 4686.3 | 96815 | 1382 | 7920-4 | 32692-0 |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1. | Baitarani | 1971 | Akhuapada | 63.00 | 59.00 | 100005 ha | 63.00 71232 ha | 59.00 35616 ha | 21-7-71 | 21-7-71 22-7-71 8-8-71 30-8-71 | Nil |
|  |  | 1972 |  | 63.00 | 59.00 | 66.20 99887 ha | 63.00 71232 ha | 59.00 35616 ha | 15-7-72 | 15-7-72 14-8-72 | Nil |
|  |  | 1973 |  | 63.00 | 59.00 | 67.80 100069 ha | 63.00 71232 ha | 59.00 35616 ha | 20-7-73 | 20-7-73 19-8-73 26-8-73 2-9-73 25-9-73 | Nil |
|  |  | 1974 |  | 63.00 | 59.00 | 67.70 100069 ha | 63.00 71232 ha | 59.00 35616 ha | 15-8-74 | 15-8-74 | Nil |
|  |  | 1975 |  | 63.00 | 59.00 | 70.00 118721 ha | 63.00 71232 ha | 59.00 35616 ha | 12-8-75 | 12-8-75 18-8-75 | Nil |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 1. | Baitarani | 1971 | Akhuapada | 63.00 | 59.00 | 21-7-71/12hrs to 22-7-71/6 hrs = 18/2 days |  |  |
|  |  |  |  |  |  | 27-7-71/18 hrs to 30-7-71/ 6 hrs = 60 hrs/3 days |  |  |
|  |  |  |  |  |  | 8-8-71/6 hrs to 12-8-71/6 hrs = 96 hrs/ 5 days |  |  |
|  |  |  |  |  |  | 30-8-71/9 hrs to 31-8-71/24hrs = 40 hrs/ 2 days |  |  |
|  |  | 1972 |  | 63.00 | 59.00 | 15-7-72/5 hrs to 16-7-72/9 hrs = 28 hrs/2 days | 11-9-72/12 hrs to 15-9-72/6 hrs = 90 hrs/5 days |  |
|  |  |  |  |  |  | 14-8-72/6 hrs to 15-8-72/18 hrs= 36 hrs/ 2 days |  |  |
|  |  | 1973 |  | 63.00 | 59.00 | 20-7-73/12 hrs to 23-7-73/7 hrs = 67 hrs/ 4 days | 2-9-73/15 hrs to 6-9-73/6 hrs = 87 hrs /5 days |  |
|  |  |  |  |  |  | 19-8-73/2 hrs to 21-8-73/ = 58 hrs/ 3 days | 25-9-73/6 hrs to 26-9-73/9 hrs = 27 hrs/ 2 days |  |
|  |  |  |  |  |  | 26-8-73/20 hrs to 29-8-73/18 hrs = 70 hrs/ 4 days |  |  |
|  |  | 1974 |  | 63.00 | 59.00 | 15-8-74/18 hrs to 18-8-74/11 hrs = 65 hrs /4 days |  |  |
|  |  | 1975 |  | 63.00 | 59.00 | 12-8-75/18 hrs to 14-8-75/11 hrs = 48 hrs/ 3 days |  |  |
|  |  |  |  |  |  | 18-8-75/21 hrs to 22-8-75/6 hrs = 82 hrs/ 5 days |  |  |
| Annexure2.2 |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 1 | Baitarani | 1976 | Akhuapada | 63.00 | 59.00 | 61.10/ 51673 ha | 63.00/ 71232 ha | 59.00/ 35616 ha | 14-8-76 | 14-8-76 | Nil |
|  |  | 1977 |  | 63.00 | 59.00 | 59.80/ 49976 ha | 63.00/ 71232 ha | 59.00/ 35616 ha | 7-8-77 | 7-8-77 1-9-77 | Nil |
|  |  | 1978 |  | 63.00 | 59.00 | 64.00/ 87476 ha | 63.00/ 71232 ha | 59.00/ 35616 ha | 28-8-78 | 28-8-78 2-9-78 22-9-78 | Nil |
|  |  | 1979 |  | 63.00 | 59.00 | 65.15/ 88679 ha | 63.00/ 71232 ha | 59.00/ 35616 ha | 8-8-79 | 8-8-79 | Nil |
|  |  | 1980 |  | 63.00 | 59.00 | 59.75/ 50076 ha | 63.00/ 71232 ha | 59.00/ 35616 ha | 20-9-80 | 20-9-80 | Nil |
| 2 | Brah-mani | 1971 | Joaapur Anicut | 66.00 | 62.00 | 72.30/ 195300 ha | 66.00/ 119880 ha | 62.00/ 59400 ha | 14-7-71 | 14-7-71 16-7-71 27-7-71 29-7-71 1-8-71 | 14-7-71/12 hrs to 15-7-71 24 hrs. = 36 hrs. (2 days) |
|  |  | 1972 |  | 66.00 | 62.00 | 67.90/ 89278 ha | 66.00/ 119880 ha | 62.00/ 59400 ha | 15-7-72 | 15-7-72 12-9-72 | Nil |
|  |  | 1973 |  | 66.00 | 62.00 | 73.10/ 168006 ha | 66.00/ 119880 ha | 62.00/ 59400 ha | 20-7-73 | 20-7-73 20-8-73 27-8-73 3-9-73 25-9-73 28-10-73 | Nil |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 1. | Baitarani | 1976 | Akhuapada | 63.00 | 59.00 | 14-8-76/8 hrs to 15-8-76/18 hrs = 34 hrs/ 2 days |  |  |
|  |  | 1977 |  | 63.00 | 59.00 | 7-8-77/1 hrs to 8-8-77/0 hrs = 24 hrs/ 2 days | 1-9-77/0 hrs to 2-9-77/6 hrs = 30 hrs/ 2 days |  |
|  |  | 1978 |  | 63.00 | 59.00 | 28-8-78/12 hrs to 30-8-78/12 hrs = 48 hrs/3 days | 2-9-78/15 hrs to 3-9-78/6 hrs = 15 hrs |  |
|  |  |  |  |  |  |  | 22-9-78/6 hrs to 23-9-78/24 hrs = 48 hrs |  |
|  |  | 1979 |  | 63.00 | 59.00 | 8-8-79/7 hrs to 11-8-79/2 hrs = 67 hrs | Nil |  |
|  |  | 1980 |  | 63.00 | 59.00 | Nil | 20-9-80/00 hrs to 21-9-80/1 hrs = 24 hrs/1 day |  |
| 2. | Brah-mani | 1971 | Joaapur Anieut | 66.00 | 62.00 | 16-7-71/0 hrs to 25-7-71/12 hrs = 228 hrs/10 days | 1-9-71/00 hrs to 11-9-71/9 hrs = 249 hrs/ 11 days |  |
|  |  |  |  |  |  | 27-7-71/15 hrs to 24-8-71/6 hrs = 687 hrs/ 29 days |  |  |
|  |  |  |  |  |  | 29-8-71/6 hrs to 31-8-71/24 hrs = 66 hrs/3 days |  |  |
|  |  | 1972 |  | 66.00 | 62.00 | 15-7-72/6 hrs to 17-7-72/12 hrs = 54 hrs/3 days | 12-9-72/56 hrs to 15-9-72/8 hrs = 82 hrs/ 4 days |  |
|  |  | 1973 |  | 66.00 | 62.00 | 20-7-73/7 hrs to 22-7-73/12 hrs = 53 hrs/3 days | 3-9-73/15 hrs to 8-9-73 /8 hrs = 114 hrs/ 6 days |  |
|  |  |  |  |  |  | 20-8-73/3 hrs to 24-8-73/6 hrs = 99 hrs/5 days | 25-9-73/6 hrs to 30-9-73/6 hrs = 108 hrs/ 6 days |  |
|  |  |  |  |  |  | 27-8-73/6 hrs to 31-8-73/9 hrs = 99 hrs/ 5 days | 8-10-73/6 hrs to 31-10-73/6 hrs = 72 hrs/ 4 days |  |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 2. | Brahmani | 1974 | Jonapur Anicut | 66.00 | 62.00 | 69.50 113501 ha | 66.00 119880 ha | 62.00 59400 ha | 14-8-74 | 14-8-74 | Nil |
|  |  | 1975 |  | 66.00 | 62.00 | 75.20 199800 ha | 66.00 119880 ha | 62.00 59400 ha | 19-7-75 | 19-7-75 10-8-75 | Nil |
|  |  | 1976 |  | 66.00 | 62.00 | 68.60 110055 ha | 66.00 119880 ha | 62.00 59400 ha | 20-7-76 | 20-7-76 31-7-76 13-8-76 19-9-76 | Nil |
|  |  | 1977 |  | 66.00 | 62.00 | 68.40 110007 ha | 66.00 119880 ha | 62.00 59400 ha | 5-7-77 | 5-7-77 31-7-77 1-9-77 10-9-77 | 5-7-77/88 hrs. to 9-7-77/9 hrs= 87 hrs./5 days |
|  |  | J9.78 |  | 66.00 | 62.00 | 66.80 101430 ha | 66.00 119880 ha | 62.00 59400 ha | 30-6-78 | 30-6-78 31-7-78 5-8-78 13-8-78 28-8-78 3-9-78 | 30-6-78 / 03 hrs to 30-6-78/ 18 hrs = 12 hrs /1 day |
|  |  | 1979 |  | 66.00 | 62.00 | 66.70 101416 ha | 66.00 119880 ha | 62.00 59400 ha | 8-8-79 | 8-8-79 | Nil |
|  |  | 1980 |  | 66.00 | 62.00 | 63.20 55376 ha | 66.00 119880 ha | 62.00 59400 ha | 22-6-80 | 22-6-80 25-6-80 8-9-80 | 22-6-80/ 03 hrs to 23-6-80/ 06 hrs = 27 hrs/2 days 25-6-80/0 hrs to 26-6-80/ 06 hrs = 30 hrs /2 days |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 2. | Brahmani | 1974 | Jonapur Anicut | 66.00 | 62.00 | 14-8-74/8 hrs to 21-8-74 = 181 hrs/8 days |  |  |
|  |  | 1975 |  | 66.00 | 62.00 | 19-7-75/6 hrs to 23-7-75/18 hrs = 108 hrs/5 days |  |  |
|  |  |  |  |  |  | 10-8-75/9 hrs to 26-8-75/6 hrs = 381 hrs/17 days |  |  |
|  |  | 1976 |  | 66.00 | 62. 00 | 20-7-76/18 hrs to 21-7-76/12 hrs= 18 hrs/ 2 days |  |  |
|  |  |  |  |  |  | 31-7-76/18 hrs to 1-8-76/24 hrs = 30 hrs/ 2 days |  |  |
|  |  |  |  |  |  | 13-8-76/18 hrs to 17-8-76/18 hrs = 96 hrs/ 5 days | 19-9-76 to 22-9-76 = 72 hrs 03 hrs 03 hrs 4 days |  |
|  |  | 1977 |  | 66.00 | 62.00 | 31-7-77/9hrs to 13-8-77/3 hrs = 307 hrs/ 14 days | 1-9-77 to 3-9-77 = 66 hrs 00 hrs 18 hrs . 3 days |  |
|  |  |  |  |  |  |  | 10-9-77/0 hrs to 13-9-77/18 hrs = 96 hrs/ 3 days |  |
|  |  | 1978 |  | 66.00 | 62.00 | 31-7-78/18 hrs to 1-8-78/18 hrs = 24 hrs / 2 days | 3-9-78/3 hrs to 7-9-78/18 hrs = 111 hrs/ 5 days |  |
|  |  |  |  |  |  | 5-8-78/0 hrs to 6-8-78/18 hrs = 42 hrs/ 2 days |  |  |
|  |  |  |  |  |  | 13-8-78 /6 hrs to 16-8-78/6 hrs = 72 hrs/ 4 days |  |  |
|  |  |  |  |  |  | 28-8-78/0 hrs to 30-8-78/18 hrs = 66 hrs/ 3 days |  |  |
|  |  | 1979 |  | 66.00 | 62.00 | 8-8-79/18 hrs to 12-8-79/18 hrs = 87 hrs/5 days |  |  |
|  |  | 1980 |  | 66.09 | 62.00 | Nil | 8-9-80/18 hrs to 9-9-80/24 hrs = 30 hrs/ 2 days |  |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 3. | Burhabalanga | 1971 | Fuladi | 14.50 +9.50 = 24.00 RL | 10.50 | 14.20 41210 ha | 14.50 44346 ha | 10.50 22170 ha | 8-8-71 | 8-8-71 (Max) 28-8-71 5-9-71 | Nil |
|  |  | 1972 |  | -do- | 10.50 | 14.80 457210 ha | 14.50 44346 ha | 10.50 22170 ha | 13-8-72 | 13-8-72 11-9-72 25-9-72 | Nil |
|  |  | 1973 |  | -do- | 10.50 | 19.50 11275 ha | 14.50 44346 ha | 10.50 22170 ha | 21-7-73 | 21-7-73 27-8-73 1-9-73 22-9-73 12-10-73 | Nil |
|  |  | 1974 |  | -do- | 10.50 | 15.80 73910 ha | 14.50 44346 ha] | 10.50 22170 ha | 16-8-74 | 16-8-74 | Nil |
|  |  | 1975 |  | 24.00 | 10.50 | 15.40 71205 ha | 14.50 44346 ha | 10.50 22170 ha | 12-8-75 | 12-8-75 19-8-75 9-9-75 | Nil |
|  |  | 1976 |  |  | -do- | 13.20 38060 ha | 14.60 44346 ha | 10.50 22170 ha | 4-8-76 | 4-8-76 12-9-76 | Nil |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 3. | Burhabalanga | 1971 | Fuladi | 14.50 + 9.50 = 24. 00RL | 10.50 | 8-8-71/12 hrs to 11-8-71/12 hrs = 72hrs/ 3 days | 5-9-71/12 hrs to 7-9-71/18 hrs = 54 hrs/ 3 days |  |
|  |  |  |  |  |  | 28-8-71/6 hrs to 31-8-71/18 hrs = 84 hrs/ 4 days |  |  |
|  |  | 1972 |  |  | 99 | 13-8-72/18 hrs to 15-8-72/18 hrs = 48 hrs/ 2 days | 11-9-72/6 hrs to 16-9-72/6 hrs = 120 hrs/ 5 days |  |
|  |  |  |  |  |  |  | 25-9-72/6 hrs to 26-9-72/6 hrs = 24 hrs/ 1 day |  |
|  |  | 1973 |  | 99 |  | 21-7-73/6 hrs to 22-7-73/15 hrs = 33 hrs/ 2 days | 1-9-73/6 hrs to 5-9-73/24 hrs = 114 hrs/ 5 days |  |
|  |  |  |  |  |  | 27-8-73/12 hrs to 29-8-73/6 hrs = 42 hrs/ 2 days | 22-9-73/18 hrs to 27-9-73/7 hrs = 109 hrs/ 5 days |  |
|  |  |  |  |  |  |  | 12-10-73/0 hrs to 15-10-73/7 hrs = 79 hrs/ 4 days |  |
|  |  | 1974 |  |  | 99 | 16-8-74/0 hrs to 19-8-74/12 hrs = 84 hrs/ 4 days |  |  |
|  |  | 1975 |  | 99 |  | 12-8-75/7 hrs to 13-8-75/8 hrs = 25 hrs/ 1 day | 9-9-75/0 hrs to 14-9-75/4 hrs = 124 hrs/ 4 days |  |
|  |  |  |  |  |  | 19-8-75/0 hrs to 23-8-75/7 hrs = |  |  |
|  |  | 1976 |  |  | 99 | 4-8-76/22 hrs to 6-8-76/24 hrs = 50 hrs/ 3 days | 12-9-76/3 hrs to 15-9-76/5 hrs = 74 hrs/ 4 days |  |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 3. | Burhabalanga | 1977 |  | 14.50 +9.50 = 24.00 RL | 10.50 | 13.80 38750 ha | 14.50 44346 ha | 10.50 22170 ha | 30-7-77 | 30-7-77 4-8-77 30-8-77 1-9-77 13-9-77 | Nil |
|  |  | 1978 |  | 14.50 | 10.50 | 14.60 44560 ha | 14.50 44346 ha | 10.50 22170 ha | 15-8-78 | 15-8-78 24-8-78 1-9-78 18-9-78 22-9-78 4-10-78 | Nil |
|  |  | 1979 |  | 14.50 | 10.50 | 14.60 4560 ha | 14.50 44346 ha | 10.50 22170 ha. | 8-8-79 | 8-8-79 | Nil |
|  |  | 1980 |  | 14.50 | 10.50 | 11.40 30510 ha | 14.50 44346 ha | 10.50 22170 ha | 21-6-80 | 21-6-80 8-9-80 18-9-80 | 21-6-80/18 hrs to 21-6-80/21 hrs = 3 hrs |
| 4. | Subranarekha | 1971 | Rajaghat | 15.00 | 11.00 | 18.40 42970 ha | 15.00 32850 ha | 11.00 16425 ha | 15-7-71 | 15-7-71 27-7-71 2-8-71 30-8-71 1-9-71 | Nil |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 3. | Burhabalanga | 1977 |  | 14.50 +9.50 = 24.00 RL | 10.50 | 30-7-77/11 hrs to 1-8-77/7 hrs = 44 hrs/ 3 days |  |  |
|  |  |  |  |  |  | 4-8-77/11 hrs to 10-8-77/24 hrs = 157 hrs/ 7 days |  |  |
|  |  |  |  |  |  | 30-8-77/4 hrs to 31-8-77/24 hrs = 44 hrs | 1-9-77/0 hrs to 3-9-77/13 hrs = 13 hrs/ 3 days |  |
|  |  |  |  |  |  |  | 13-9-77/3 hrs to 14-9-77/9 hrs = 30 hrs/ 2 days |  |
|  |  | 1978 | Fuladi | 14.50 | 10. 50 | 15-8-78/16 hrs to 19-8-78/24 hrs = 104 hrs/ 5 days | 1-9-78/0 hrs to 4-9-78/18 hrs = 90 hrs/ 4 days |  |
|  |  |  |  |  |  | 24-8-78/11 hrs to 31-8-78/24 hrs = 181 hrs/7 days | 18-9-78/6 hrs to 19-9-78/18 hrs = 36 hrs/2 days |  |
|  |  |  |  |  |  |  | 22-9-78/6 hrs to 24-9-78/18 hrs = 66 hrs/3 days |  |
|  |  |  |  |  |  |  | 4-10-78/12 hrs to 7-10-78/12 hrs = 72 hrs/ 3 days |  |
|  |  | 1979 |  | 14.50 | 10.50 | 8-8-79 / 6 hrs to 10-8-79/16 hrs = 58 hrs/3 days | Nil |  |
|  |  | 1980 |  | 14.50 | 10.50 |  | 8-9-80/7 hrs to 8-9-80/17 hrs = 10 hrs |  |
|  |  |  |  |  |  |  | 18-9-80/6 hrs to 19-9-80/18 hrs = 36 hrs/ 2 days |  |
| 4. | Subranarekha | 1971 | Rajghat | 15.00 | 11.00 | 15-7-71= 1 day |  |  |
|  |  |  |  |  |  | 27-7-71/6 hrs to 31-7-71/6 hrs= 96 hrs/5 days | 1-9-71/0 hrs to 9-9-71/24 hrs = 216 hrs/ 9 days |  |
|  |  |  |  |  |  | 2-8-71/0 hrs to 16-8-71/0 hrs= 360 hrs/15 days |  |  |
|  |  |  |  |  |  | 30-8-71/0 hrs to 31-8-71/24 hrs = 48 hrs/ 2 days |  |  |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No | Name of river | Year | Gauge site (O. value of to gauge (—) 1.28) | Danger level | Flood Spilling level | Area Flooded | Year (10 years from 1971 to 1980) |
|  |  |  |  |  |  | Maximum gauge | Danger level | Low gauge 4'-0 below danger level | When flooding started | Date of flooding | Incidence of earlier flood upto 15th July dates and duration |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| 4 | Subranarekba | 1972 | Rajghat | 15.00 | 11.00 | 18.50/ 42976 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 14-8-72 | 14-8-72 12-9-72 | Nil |
|  |  | 1973 |  | 15.00 | 11.00 | 20.30/ 39.30/ RL 54750 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 20-8-73 | 20-8-73 1-9-73 24-9-73 12-10-73 | Nil |
|  |  | 1974 |  | 15.00 | 11.00 | 19.80/ 48750 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 16-8-74 | 16-8-74 30-9-74 | Nil |
|  |  | 1975 |  | 15.00 | 11.00 | 19.80/ 48750 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 19-7-75 | 19-7-75 13-8-75 | Nil |
|  |  | 1976 |  | 15.00 | 11.00 | 19.00/ 47097 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 13-9-76 | 13-9-76 18-9-76 | Nil |
|  |  | 1977 |  | 15.00 | 11.00 | 20.00/ 54600 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 15-7-77 | 15-7-77 30-7-77 | Nil |
|  |  | 1978 |  | 15.00 | 11.00 | 20.80/ 55745 ha | 15.00/ 32850 ha | 11.00/ 16425 ha | 29-8-78 | 29-8-78 2-9-78 28-9-78 6-10-78 | Nil |
|  |  | 1979 |  | 15.00 | 11.00 | No remarks flood between D.L. Hence nil |  |  |
|  |  | 1980 |  | 15.00 | 11.00 | No remarks flood between D.L. Hence nil |  |  |

| Annexure2.2 |
| --- |
| FREQUENCY AND INCIDENCE OF FLOODING IN SOME RIVERS OF ORISSA |
| SI. No. | Name of River | Year | Gauge site (O. value of to gauge (—) 1-28) | Danger level | Flood Spilling level | Incidence of other floods (from 15th July to 30th August) Date and Duration | Incidence of Flood (from September to October) Dates and Duration | REMARKS |
| 1 | 2 | 3 | 4 | 5 | 6 | 13 | 14 | 15 |
| 4. | Subranarekha | 1972 |  | 15.00 | 11.00 | 14-8-72/7 hrs to 16-8-72/9 hrs = 50 hrs/3 days | 12-9-72/8 hrs to 14-9-72/12 hrs = 52 hrs/3 days |  |
|  |  | 1973 |  | 15.00 | 11.00 | 20-8-73 | 1-9-73 /0 hrs to 6-9-73/24 hrs = 144 hrs/ 6 days |  |
|  |  |  |  |  |  |  | 24-9-73/0 hrs to 28-9-73/15 hrs = 111hrs/5 days |  |
|  |  |  |  |  |  |  | 12-10-73/18 hrs to 17-10-73/10 hrs = 112 hrs/ 6 days |  |
|  |  | 1974 | Rajghat | 15.00 | 11.00 | 16-8-74/6 hrs to 21-8-74/6 hrs = 120 hrs/6 days | 30-9-74/13 hrs to 2-10-74/24 hrs = 83 hrs/3 days |  |
|  |  | 1975 |  | 15.00 | 11.00 | 19-7-75 = 1 day |  |  |
|  |  |  |  |  |  | 13-8-75/14 hrs to 24-8-75/19 hrs = 269 hrs/12 days |  |  |
|  |  | 1976 |  | 15.00 | 11.00 | Nil | 13-9-76/10 hrs to 14-9-76/24 hrs = 38 hrs/2 days |  |
|  |  |  |  |  |  |  | 18-9-76/16 hrs to 22-9-76/19 hrs = 99 hrs/5 days |  |
|  |  | 1977 |  | 15.00 | 11.00 | 15-7-77/11 hrs to 17-7-77/11 hrs = 48 hrs/2 days |  |  |
|  |  |  |  |  |  | 30-7-77/9 hrs to 11-8-77/16 hrs = 295 hrs/13 days |  |  |
|  |  | 1978 |  | 15.00 | 11.00 | 29-8-78/7 hrs to 31-8-78/16 hrs = 67hrs/ 3 days | 2-9-78/3 hrs to 6-9-78/24 hrs = 117 hrs/ 5 days |  |
|  |  |  |  |  |  |  | 28-9-78 =1day 6-10-78 = 1 day |  |

| annexure 2.3 |
| --- |
| IINCIDENCE OF EARLIEST LATEST & LATEST BUT ONE FLOODS IN MAJOR RIVERS OF UTTAR PRADESH DURING LAST FIVE YEARS |
| Name of River | Gauge site | Danger level in Meters | Ever maximum flood level in meters with year | YEAR 1975 |
|  |  |  |  | Incidence of earlier floods (when the river crossed danger level) | Incidence of other latest floods (when the river crossed danger level) | Incidence of other floods (when the river crossed danger level) |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| 1. Ganga | Hardwar | 294.00 | 295.78 (1978) |  |  |  |
| 2. Ganga | Narora D/S | 178.40 | 180.20 (1924) | 21-7-75 (1 day) | 9-9-75 (1 day) |  |
| 3. Ganga | Phaphamau | 84.73 | 88.39 (1948) |  |  |  |
| 4. Ganga | Chatnag | 84.73 | 88.39 (1948) |  |  |  |
| 5. Ganga | Mirzapur | 77.72 | 79.53 (1971) |  |  |  |
| 6. Ganga | Rajghat (Varanasi) | 71.26 | 76.61 (1977) |  |  |  |
| 7. Ganga | Ghazipur | 63.105 | 64.37 (1971) |  |  |  |
| 8. Ganga | Ghaighat Ballia | 56.39 | 58.65 | 25-7-75 (1 day) | 11 to 21-9-75 (11 days) | 11-8-75 to 13, 21 to 30-8-75 (6 days) |
| 9. .Yamuna | Delhi Bridge | 204.83 | 207.50 (1978) | 26-7-75(1 day) | 14-9-75 |  |
| 10. Yamuna | uriya | 108.95 | 109.02 (1978) |  |  |  |
| 11. Yamuna | Hamirpur | 104.24 | 108.140 (1978) |  |  |  |
| 12. Yamuna | Chillaghat | 100.00 | 106.34 (1967) |  |  |  |
| 13. Yamuna | Naini | 84.73 | 87.98 (1978) |  |  |  |
|  | Allahabad |  |  |  |  |  |
| 14. Gomti | Ghaighat | 110.49 | 113.20 (1960) | 20-6-75 | 27-8 to 18-9-75 | (11 days) |
|  | Lucknow |  |  |  | 123 days) |  |
| 15. Gomti | Jaunpur | 74.06 | 77.74 (1971) |  |  |  |
| 16. Sarda | Paliakalan Kheiri | 153.619 | 154.80 (1975) | 23 & 24-6-75 | 5 to 22-9-76 |  |
|  | Kheiri |  |  | (2 days) | (18 days) | (46 days) |
| 17. Sarda | Sardanagar | 135.49 | 135.95 (1969) |  |  |  |
|  | Kheiri |  |  |  |  |  |
| 18. Ghaghra | Katarnia Ghat | 136.78 | 137.00 (1970) |  |  |  |
|  | Baharaich |  |  |  |  |  |
| 19. Ghaghra | Elginbridge (Barabanki) | 106.078 | 107.88 (1950) | 24 .6 to 10-7-75 (17 days) | 6 to 13-9-75 (8 days) | (26 days) |
| 20. Ghaghra | Ayodhya | 92.73 | 94.08 (1971) |  |  |  |
| 21. Ghaghra | Turitipar Ballia | 64.01 | 65.16 (1975) | 3 to 7-7-75 | 23.8 to 20-9-75 | (21 days) |
| 22. Rapti | Kakardhari | 131.00 | 130.16 (1978) |  |  |  |
| 23. Rapti | Balrampur Gonda | 104.62 | 105.90 (1969) |  |  |  |
| 24. Rapti | Bansi (Basti) | 84.90 | 87.44 (1966) |  |  |  |
| 25. Rapti | Birdghat Gorakhpur | 74.98 | 76.63 (1925) | 11-7-75 | 9 to 16-9-75 | (24 days) |
| 26. Burhi Rapii | Kakrahi | 85.679 | 87.465 (1978) | 1 to 14-7-75 | 6 to 13-9-75 | (30 days) |
| 27.Grade Gandak | Bhainsa | 96.00 | 96.85 (1978) | 2-7-75 | 9-10-75 | (12 days) |
| 28. Tons | Azamgarh | 74.725 | 75.08 (1980) |  |  |  |

| annexure 2.3 |
| --- |
| IINCIDENCE OF EARLIEST LATEST & LATEST BUT ONE FLOODS IN MAJOR RIVERS OF UTTAR PRADESH DURING LAST FIVE YEARS |
| Name of River | Gauge Site | Year 1976 | Year 1977 |
|  |  | Incidence of earliest floods (when the river crossed danger level) | Incidence of latest floods (when the river crossed danger level) | Incidence of other floods (when the river crossed danger level) | Incidence of earliest floods (when the river crossed danger level) | Incidence of latest floods (when the river crossed danger level) | Incidence of other floods (when the river crossed danger level) |
| 1 | 2 | 8 | 9 | 10 | 11 | 12 | 13 |
| 1. Ganga | Hardwar |  |  |  |  |  |  |
| 2. Ganga | Narora D/S | 29-7-76 (1 day) | 22-8-76 |  |  |  |  |
| 3. Ganga | Phaphamau |  |  |  |  |  |  |
| 4. Ganga | Chatnag |  |  |  |  |  |  |
| 5. Ganga | Mirzapur |  |  |  |  |  |  |
| 6. Ganga | Pajghat (Varanasi) | 14 & 15-9-76 (2 days) |  |  |  |  |  |
| 7. Ganga | Ghazipur |  |  |  | 10 & 11-7-77 (2 days) | 6-9-77 (1 day) | 2 & 4-9-77 (2 days) |
| $. Ganga | Ghaighat Ballia | 19-8-76 (1 day) | 12 to 23-9-76 (12 days) |  | 1 to 16-8-77 (16 days) | 19 to 23-9-77 (5 days) | 3, 5 & 13-8-77 (3 days) |
| 9. Yamuna | Delhi Bridge | 2 & 3-8-76 (2 days) | 20 to 8-76 (7 days) | 8 to 14-8-76 (6 days) | 28 to 29-7-77 (2 days) | 14 to 17-9-77 (2 days) | 3, 5, 13-8-77 (3 days) |
| 10. Yamuna | Auriya |  |  |  |  |  |  |
| 11. Yamuna | Harnirpur |  |  |  |  |  |  |
| 12. Yamuna | Chillaghat (Banda) |  |  |  |  |  |  |
| 13. Yamuna | Naini (Allahabad) |  |  |  |  |  |  |
| 14. Gomti | Ghaighat (Lucknow) |  |  |  |  |  |  |
| 15. Gomti | Jaunpur |  |  |  |  |  |  |
| 16. Sarda | Paliakalan Kheiri |  |  |  |  |  |  |
| 17. Sarda | Sardanagar Kheiri |  |  |  |  |  |  |
| 18. Ghaghra | Katarnia Ghat, Batyaraich |  |  |  |  |  |  |
| 19. Ghaghra | ElginbridgBarabanki | 19 to 28-8-76 (10 days) | 11-9-76 |  |  | 17-7-77 | 14 to 16-9-77 |
| 20. Ghaghra | Ayodhya |  |  |  |  |  |  |
| 21. Ghaghra | Turtipar Ballia | 20 to 3 1-8-76 |  |  |  | 19 to 22-8-77 | 29-8 to 4-9-77 |
| 22. Rapti | Kakardhar |  |  |  |  |  |  |
| 23. Rapti | Balrampur (Gonda) |  |  |  |  |  |  |
| 24. Rapti | Bansi (Basti) |  |  |  |  |  |  |
| 25. Rapti | Birdghat |  |  |  |  |  |  |
|  | Gorakhpur |  |  |  |  |  |  |
| 26. Burhi Rapti | Kakrahi | 24 to 27-8-76 |  |  |  | 26-8 to 4-9-77 |  |
| 27. Grade Gandak | Bhainsa | 24-8-76 |  |  |  | 27 to 30-8-77 | 13 to 15-9-77 |
| 28. Tons | Azamgarh |  |  |  |  |  |  |

| annexure 2.3 |
| --- |
| IINCIDENCE OF EARLIEST LATEST & LATEST BUT ONE FLOODS IN MAJOR RIVERS OF UTTAR PRADESH DURING LAST FIVE YEARS |
| Name of River | Gauge Ghate | Year 1978 | Year 1980 |
|  |  | Incidence of earliest floods (when the river crossed danger level) | Incidence of latest floods (when the river crossed danger level) | Incidence of other floods (when the river crossed danger level) | Incidence of earliest floods (when the river crossed danger level) | Incidence of latest floods (when the river crossed danger level) | Incidence of other floods (when the river crossed danger level) |
| 1 | 2 | 14 | 15 | 16 | 17 | 18 | 19 |
| 1. Ganga | Hardwar | 2 & 3-8-78 (2 days) | 3-9-78 | 6 & 11-8-78 (2 days) |  |  |  |
| 2. Ganga | Narora D/S | 5 to 16-8-78 (12 days) | 5 to 7-9-78 (3 days) | 29 & 30-8-79 (2 days) | 3 to 12-8-80 (10 day |  |  |
| 3. Ganga | Phaphamua | 14 & 15-8-78 (2 days) | 6 & 11-9-78 (6 days) |  | 1 & 2-9-80 (2 days) |  |  |
| 4. Ganga | Chatnag | 5 to 11-9-78 (7 days) |  |  | 31-8 to 3-9-80 (6 days) |  |  |
| 5. Ganga | Mirzapur |  |  |  |  |  |  |
| 6. Ganga | Rajghat Varanasi | 14 to 16-8-78 (3 days) | 6 to 13-8-78 (8 days) |  | 30-8 to 3-9-80 (6 days) |  |  |
| 7. Ganga | Ghazipur |  |  |  | 12-8 to 5-9-80 (25 days |  |  |
| 8. Ganga | Gaighat Ballia | 9-8 to 1-9-78 (24 days) | 4 to 6-9-78 (3 days) |  | 7 to 21-8-70 (15 days) | 27-8 to 13-9-80 (18 days) |  |
| 9. Yamuna | Delhi Bridge | 11 to 12-7-78 (2 days) | 2 to 10-9-78 (9 days) | 19 days |  |  |  |
| 10. Yamuna | Auriya | 7-9-78 |  |  |  |  |  |
| 11. Yamuna | Hamirpur | 6 to 8-9-78 |  |  |  |  |  |
| 12. Yamuna | Chillaghat Banda | 5 to 9-9-78 |  |  | 29-8 to 2-9-80 (5 days) |  |  |
| 13. Yamuna | Naini (Allahabad) | 14-8-78 | 6 to 11-9-78 (6 days) |  | 31-8 to 2-9-80 (3 days) |  |  |
| 14. Gomti | Gaughat Lucknow |  |  |  | 25 & 28-7-80 (2 days) |  |  |
| 15. Gomti | Jaunpur |  |  |  | 4-8 to 15-8-80 (12 days) | 22-9 to 1-10-80 (10 days) | 17-8 to 20-9-80 (35days) |
| 16. Sarda | Paliakalan Kheiri |  |  |  |  |  |  |
| 17. Sarda | Sardanagar Kheiri | 29-8-78 |  |  |  |  |  |
| 18. Ghaghra | Katarniaghat Bahraich | 19-7-78 |  |  |  |  |  |
| 19. Ghaghra | Eliginbridge (Barabanki) | 4 to 17-7-78 (14 days) | 27 to 30-8-78 (4 days) |  | 10-7-78 (1 day) | 3 to 10-9-78 (8 days) | 18-7 to 18-8-80 (31 days) |
| 20. Ghaghra | Ayodhya |  |  |  | 6 to 10-8-80 (5 days) |  |  |
| 21. Ghaghra | Turtipar Ballia | 20 to 22-7-78 | 28 to 31-8-78 |  | 21-7 to 21-8-80 (32 days) | 24 to 26-9-80 (3 days) | 26-8 to 1-9-80 4 to 15-9-80 (19 days) |
| 22. Rapti | Kakardhari | 17-7-78 |  |  |  |  |  |
| 23. Rapti | Balrampur Gonda | 17 to 19-7-78 |  |  |  |  |  |
| 24. Rapti | Bansi (Basti) | 19 to 22-7-78 |  |  |  |  |  |
| 25. Rapti | Birdghat Gorakhpur | 21-7 to 31-8-78 |  |  | 26 to 30-9-80 (5 days) |  |  |
| 26. Barhi Rapti | Kakrahi | 17 to 25-7-78 | 8 to 11-8-78 | 30-7 to 5-8-78 |  |  |  |
| 27. Grade Gandak | Bhainsa | 17 to 18-7-78 |  |  | 1 & 2-8-80 (2 days) | 7-9-80 (1 day) | 2-9-80 (1 day) |
| 28. Tons | Azamgarh |  |  |  | 11 to 25-9-80 (15 days) |  |  |

| Annexure 2.4 |
| --- |
| FLOOD PERIOD IN DIFFERENT AREAS OF WEST BENGAL |
| Year | Period of Flood in River | Station at | MONTHS |
|  |  |  | JUN. | JUL. | AUG. | SEPT. | OCT. | TOTAL |
| l | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
|  | TEESTA | DOMOHANI |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  |  |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  |  |  |  |  |  |  |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  | 10 | 8 | 6 |  |  | 24 |
| 1975 |  |  | 7 | 10 | 4 |  |  | 21 |
| 1974 |  |  | 9 |  |  |  |  | 9 |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  | 17 | 12 | 5 |  | 5 | 39 |
|  | TEESTA | CORONATION |  |  |  |  |  |  |
| 1980 |  |  | 8 | 3 | 1 | 1 |  | 13 |
| 1979 |  |  |  | 11 |  | 2 |  | 13 |
| 1978 |  |  | 5 | 3 | 1 | 1 |  | 10 |
| 1977 |  |  | 1 | 4 | 12 |  |  | 17 |
| 1976 |  |  | 1 | 2 | 6 |  |  | 9 |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  | 5 | 21 | 8 | 4 |  | 30 |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  | 1 | 7 | 1 | 6 |  | 19 |
| 1971 |  |  | 1 | 5 |  |  |  | 6 |
|  | TORSA | GHUGUMARI |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  |  |
| 1979 |  |  |  | 2 |  |  |  | 2 |
| 1978 |  |  |  |  |  |  |  |  |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  | 1 |  |  |  | 1 |
| 1974 |  |  | 1 |  |  |  | 1 |  |
| 1973 |  |  | 1 |  |  |  | 1 | 2 |
| 1972 |  |  |  | 1 |  |  |  |  |
| 1971 |  |  |  |  |  |  |  |  |
|  | JALDHAKA | ROAD BRIDGE N.H. 31 |  |  |  |  |  |  |
| 1980 |  |  | 1 | 9 | 2 | 4 |  | 16 |
| 1979 |  |  |  | 16 | 9 | 9 |  | 34 |
| 1978 |  |  | 8 | 20 | 10 | 7 | 1 | 46 |
| 1977 |  |  |  |  | 3 | 2 | 1 | 6 |
| 1976 |  |  | 10 | 3 | 4 |  |  | 17 |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  | 4 |
| 1973 |  |  | 2 |  |  |  |  | 2 |
| 1972 |  |  |  |  |  |  |  | 2 |
| 1971 |  |  |  |  |  |  |  |  |

| Annexure 2.4 |
| --- |
| FLOOD PERIOD IN DIFFERENT AREAS OF WEST BENGAL |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
|  | MOHANDNDRA | FULBARI |  |  |  |  |  |  |
| 1980 |  |  |  | 1 |  |  |  | 1 |
| 1979 |  |  |  | 1 |  | 1 |  | 2 |
| 1978 |  |  |  |  |  |  |  |  |
| 1977 |  |  |  |  | 1 |  |  | 1 |
| 1976 |  |  | 1 |  |  |  |  | 1 |
| 1975 |  |  |  | 1 |  |  |  | 1 |
| 1974 |  |  |  | 2 |  |  |  | 2 |
| 1973 |  |  |  | 1 | 2 |  |  | 3 |
| 1972 |  |  |  | 1 | 2 |  |  | 3 |
| 1971 |  |  |  | 1 |  |  |  | 1 |
|  | MAHANANDA | ENGLISHBAZAR |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  |  |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  |  |  |  |  |  |  |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  | 6 |  |  | 6 |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  | 26 | 26 |  | 52 |
| 1971 |  |  |  |  |  |  |  |  |
|  | GANGA | MANIKCHAK GHAT |  |  |  |  |  |  |
| 1980 |  |  |  |  | 2 |  |  | 2 |
| 1979 |  |  |  |  | 31 | 26 |  | 57 |
| 1978 |  |  |  |  | 21 | 6 |  | 27 |
| 1777 |  |  |  |  | 13 | 16 |  | 29 |
| 1976 |  |  |  |  | 16 | 14 |  | 30 |
| 1975 |  |  |  |  | 31 | 6 |  | 37 |
| 1974 |  |  |  | 2 | 21 |  |  | 23 |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  |  | 9 | 31 | 23 |  | 63 |
|  | GANGA | NURPUR |  |  |  |  |  |  |
| 1980 |  |  |  | 12 | 31 | 19 |  | 62 |
| 1979 |  |  |  | 3 | 8 |  |  | 11 |
| 1978 |  |  |  |  | 17 | 18 |  | 45 |
| 1977 |  |  |  |  | 20 |  |  | 20 |
| 1976 |  |  |  |  | 11 | 14 |  | 25 |
| 1975 |  |  |  | 3 | 20 | 14 |  | 37 |
| 1974 |  |  |  |  | 19 | 4 |  | 23 |
| 1973 |  |  |  |  | 13 | 20 |  | 33 |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  |  | 8 | 31 | 22 |  | 61 |
|  | BHAGIRATHI | BERHAMPORE |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  |  |
| 1979 |  |  |  |  | 5 | 7 | 1 | 13 |
| 1978 |  |  |  |  |  |  |  |  |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |

| Annexure 2.4 |
| --- |
| FLOOD PERIOD IN DIFFERENT AREAS OF WEST BENGAL |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  |  |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  | 31 | 21 |  | 52 |
| 1971 |  |  |  |  |  |  |  |  |
|  | BHAGIRATHI | KA7WA |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  |  |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  |  |  |  | 2 | 11 | 13 |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  |  |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  |  |  | 9 | 30 | 14 | 53 |
|  | CHDRNT | HANSKHAL |  |  |  |  |  |  |
| 1980 |  |  |  |  | 5 | 30 | 4 | 39 |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  |  |  |  | 13 | 26 | 39 |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  |  |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  |  |  | 23 | 30 | 3 | 66 |
|  | AJOY | KATWA |  |  |  |  |  |  |
| 1980 |  |  |  |  |  |  |  | 3 |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  | 1 | 2 |  | 12 |  | 15 |
| 1977 |  |  |  |  |  |  |  |  |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  |  |
| 1973 |  |  |  |  |  |  |  |  |
| 1972 |  |  |  |  |  |  |  |  |
| 1971 |  |  |  | 12 | 18 | 11 |  | 41 |
|  | JALANGL | SWARUPGANJ |  |  |  |  |  |  |
| 1980 |  |  |  |  | 5 | 26 |  | 31 |
| 1979 |  |  |  |  |  |  |  |  |
| 1978 |  |  |  |  | 22 | 30 | 22 | 74 |
| 1977 |  |  |  | 10 | 23 |  |  | 33 |
| 1976 |  |  |  |  |  |  |  |  |
| 1975 |  |  |  |  |  |  |  |  |
| 1974 |  |  |  |  |  |  |  |  |
| 1973 |  |  |  |  |  | 7 | 2 | 9 |
| 1972 |  |  |  |  |  | 7 | 2 | 9 |
| 1971 |  |  |  | 2 | 31 | 27 |  | 60 |

# 3. CROPPING STRATEGY

3.1 According to the Government reports, 40 million hectares of land are generally liable to flood in    the country.    Of this, only 10 million hectares have    so far  been  provided  with  reasonable  flood  protection measures.    For geographical or seismic reasons,    extensive areas in the flood plains of the Ganges and the Bramhaputra river systems continue to remain chronically  flood   prone. There   are   also   situations where changes   in   river   courses   and   avulsions   make   the river flow over land, outside its natural channel    and flood extensive areas.    This is witnessed generally in the Adhvara group of rivers in north Bihar and    in the  deltaic    region  of  coastal     Orissa.      For these reasons, most of the chronically flood prone areas lie in the five States of Uttar Pradesh,    Bihar, Assam, West Bengal and Orissa.    In some of the worst flood years,   large   cropped   areas  have  been   affected   by flood  in these  States,    For instance,  during  1976-78 block of years, the cropped area affected by flood aggregates on the average to 41.05 lakh nectars annually for these States.    At the constant prices, the crop damage suffered has been valued at Rs. 7860.01 lakhs (National Flood Commission Report, 1980, Vol. I page 62).    Such magnitude of flood damage to cropped area in these States keeps the conditions of the local farmers backward and unstable.     Crop damages occur due to  both breaches and other causes.    The flood damage analysis for the year  1978, for two     subdivisions of Cuttack district of Orissa, reveals    that breaches accounted for 40 and 60 per cent respectively of the total damages (including crop damages).    An appropriate  cropping  strategy has, therefore, to    be adopted in these States for the chronically  flood prone areas.   The obvious pathways would be to popularise suitable flood escaping or flood tolerant cropping systems or intensifying crop production with irrigation in the flood free months there. Keeping these in view the Committee has dealt with some of the cropping strategies and sequences for chronically flood prone areas of these States in the following paras.

# UTTAR PRADESH

3.2 Annual floods inundate the riverine areas    to varying depths along the perennial rivers of the State. These  flooded  areas  are locally known as  'Khadir Land in the Western Districts and 'Diara Land' in the eastern districts of the State.    According to the report of the Technical Committee on 'Diara'    areas in Uttar Pradesh  and Bihar, Government of    India (1972), about 15.41 lakh hectares of Diara land    lie along the rivers like Ganga, Yamuna, Ghaghra, Sarda, Ramganga, Gomti and Kalinadi and occur largely in the districts of Ballia, Ghazipur, Allahabad, Farukha-bad and Etah.    With reference to the river channel and the location, the 'Diara Land' has been classified as (i) river bed 'Diara' (ii) main land 'Diara' and (iii) upland 'Diara'.    The river bed 'Diara' with fine sand to course sand deposits generally becomes available for cultivation from  December or January to June, until  the  rains.   Extensive     cultivation  of cucurbits (melons,   bottle  gourds,  pumpkin   etc.)   and     other vegetables is practised here by taking land on lease and irrigating the crops by low lift irrigation from the river.   Lying along the banks in varying widths, the main land 'Diara' gets frequently flooded during   the rainy season.    Thereby standing crops suffer heavily. Next in contiguity lies the 'Upland Diara' in the land side, which has risen in elevation due to earlier alluvial deposits and is less frequently flooded.    Hence people practice normal agriculture in upland 'Diara' The flood free period in 'Diara' land ranges from 3 to 10 months, the period being shortest in river   bed Diara where preparatory tillage starts in January. On the main land 'Diara' the flood free period, extends from      October /November   to   June.      The   'Upland Diara'     land practises normal  agricultural except  in the exceptionally high flood years when this     land gets flooded.

3.3 On main land and upland 'Diara", sole    crop of cereals or crop mixtures with cereal and pulses or cereal and oilseeds are raised under rainfed conditions. In 'Rabi' season, mixtures of wheat and mustard, barley and gram, barley and 'Khesari' are popular. 'Khe-sari' and Lentil are also raised as sole crops. During 'Kharif , mixture of maize and jowar are grown, using early  maturing  varieties  of  60 — 70  days     duration. These crop mixtures are so chosen as to harvest them before the major floods.    The State Government recommends  'Madhukar'  and  Chakia-59  varieties     of paddy for kharif cropping in situations where flood submergence  or water logging is  experienced     upto about a week.    At some locations like the 'Karanda' 'diara' in the district of Ghazipur, intensive cropping in flood free months is becoming popular with irrigation facilities.      The  concerned  State   . Departments and a limited number of land owners have taken to direct pumping of water from the river or tubewell irrigation for such cultivation.    Farmers here,     are using  5 — 10  Horse  Power  diesel  engines  and     low-capacity pumping sets for lifting water from the neighbouring stream  or river.    The pumping installations are,  of course,  set up suitably over the  high  flood level to operate electric power. Although there exists a   popular   urge  for   intensive  crop     production   in flood free months, with modern technology and irrigation water, the  spread of this practice  in  'Diara' areas has so far been limited.   The Committee, therefore, advocates such intensive agriculture in flood free months with irrigation and an appropriate State programme for its spread may be taken up on a campaign scale.

3.4 Adequate research support needs to be provided to solve  'Diara'  land problems.    Suitable     research projects should be taken up on crop and varietal improvement,  efficient methods of village     for timely operations, efficient use of irrigation water, pests and disease management etc.   Organised marketing system to pick up the farm produce from the producers and fetch remunerative prices will go a long way to promote this cropping strategy.

3.5 Given   such    facilities,  and   subject to     local requirements, the general cropping pattern for    the chronically flood prone area should be (a) intensive 'Rabi' cropping after recession of flood water with irrigation  and raising crops  with  improved varieties of wheat, potato, peas and mustard; (b) after 'Rabi' irrigated  summer croping  (Zaid) be practised, using suitable short duration varieties  of summer    maize, mung or paddy so as to harvest the crops before rains; and (c) 'Kharif cropping, when taken up., mostly flood tolerant paddy varieties like Madhukar,     Chakia-59 etc., may be adopted.

BIHAR 2.6 The 'Diara' laud in Bihar constitutes the most flood affected areas of the State.    These land aggregate to 8.63 lakh hectares (Report of the Technical Group Diara Area, 1972, Government of India) and occur in the sub-basins of the rivers Ganga, Gandak, Burhi Gandak, Sone and Kosi.   Diara lands of Bihar afe similar, in character to those described earlier for eastern Uttar Pradesh. Based on their past experience with flood incidence and flood frequency local people practise a variety of cropping programme.   In Ganga-Sone area, flood prone areas raise 'kharif-rabi' .crop rotations  of maize-wheat, jowar-bariey,     arhar-gram, .   paddy-mustard etc.    In Gandak area, people    follow annual rotations like maize-wheat,  arhar-gram, deep water paddy-summer mung  or jute..    In  Kosi area, popular  rotations   are  paddy- wheat, 'early  maize  or black  gram-barley.    In  these    areas    farmers     are increasingly practising irrigated farming in flood free months.   Shallow tube-wells and low lift direct pumping from surface water sources are popular with the local farmers.      In    Kosi    area people    are    using bamboo tubewells for profitable cropping. For flood prone  areas  outside  'Diara'  land  a  contingent  crop plan similar to West Bengal may be adopted as is suitable to local conditions.

3.7 The various practices  in the  'Diara'  land can be applied to other chronically flood affected areas wherever  suitable.        In recognition  of the  above,     the Committee is convinced that access to irrigation water is  essential for promoting intensive crop production programmes during flood free months in chronically flood prone areas of Bihar.      Some of the profitable irrigated  cropping  sequences  in such  situations  will include (i) wheat, potato or other vegetables in 'Rabi' followed by short duration summer maize or (ii) 'Rabi' wheat or barley followed by short duration summer maize or (iii) sugarcane planted  in September /October.      Other  rotations  for  unprotected  flood  prone areas may include wheat in 'Rabi' followed by paddy in Kharif for Kosi area.      In Gandak areas wheat and gram or gram and mustard mixture followed by maize in kharif , maize and arhar mixture in kharif followed by standing arhar continuing in 'Rabi' are advocated.      la   deep  water  situations,  deep  water paddy may continue to pre-dominate in the existing locations,  depending  development  of alternate farm-- ing systems for these areas.     Adequate research support as advocated for 'Diara' lands" in Uttar Pradesh holds good for Bihar.

# ASSAM

3.8 All the districts of Sibsagar, Nowgong, Lakshim-pur,  Darrang,  Kamrup,  Goalpara and Dibruaarh  in the Bramhaputra Valley experience large scale flood . every year and suffer heavy damage to crops. Flood incidence has been observed to be worst near the con- fluence.      The annual average of crop area affected bv flood in Assam Valley has been reported to be Ii85 lakh hectares during the period  1971-78, while the maximum cropped area affected being  15.4 lakh hectares daring the same period.     These areas which are chronically flood prone may continue to lack adequate flood protection for long years to come. Hence there is an urgent need for restructuring the cropping programme to minimise crop damage and loss of production.

5.9 The National Commission on Agriculture in .its report (1976) and National    Commission on    Flood (1980) have dealt with the topic of reorienta^on of cropping system for. chronically flood prone     areas. They have favoured, a farming strategy which    can escape and/or endure flood and emphasised on cultivation during the flood free months.     The Committee also holds the similar view for restructuring the cropping strategy for such problem areas.      In    Assam Valley worst floods are experienced in the months of July and August, although in some years floods have been reported in early June or in end of September. In general, however, the cropping has to be restructured to avoid the months of July and August.

3.10 There are two kinds  of flood situations obtained in the Assam Valley.      They include the one experienced in the low lying areas and the other experienced in the riverine areas when flood flow spills over the bank.   In low lying areas, over land run off from the nearby areas  and spill, from the     natural stream channels, starts entering in May and June and stands there upto depths ranging from I to 5 meters till October * and November. Locally they are known as shallow water areas if the water depth is 1-3 meters and deep water  areas wehen water depths are  3-5 meters. In the riverine areas, floods in June damage the   standing  crops  of  'Ahu'  paddy  and  jute.     In case of early sown jute, the plant is tall enough to escape loss.    Floods in July and September are   very devastating as they seriously affected the 'Sail' paddy which is the main kharif crop and accounts for more than 75 per cent of paddy area in the valley.

3.11 Recognising the flooding pattern occuring    in the riverine areas, the appropriate cropping strategy would be to raise early 'Ahu' paddy   from   February to June, followed by late transplanted    'Sail' paddy, from    September to December.    However,    farmer's acceptance of this strategy hinges on the availability of irrigation water for early planting of Ahu and   for saving the 'Sali' paddy    from moisture stress in the valley for year round surface now irrigation due to topography, the ground water resources appear to be abundant.    It is indeed reported that in most parts of the valley ground water is available within a few meters of the surface and offers great scope for exploitation at fairly low cost.    There is already    an awareness of the State Government for such a strategy to improve crop production with irrigation and minimising flood losses.    The Department of Agriculture has    included in its programme the    popularisation of  early   Ahu  paddy  followed  by late   transplanted 'Sali' paddy among farmers.    The Department   of Irrigation is implementing a World Bank funded scheme for -extending  low  lift  irrigation  and  shallow tube-wells with which  one can assure at least one good crop for the farmers   during the flood free months. In appreciation, therefore, the Committee advocates that steos should be taken to popularise an irrigated cropping programme of early 'Ahu' paddy or jute, in the pre-flood  season, followed by late 'Sali' paddy     or 'Rabi'    wheat, mustard .or pulses in the    post-flood season.   The State efforts in* the direction need to be intensified using available high yielding varieties and technology.

3.12 In the low lying deep water areas,    farmers raise crop mixture of 'Ahu' and 'Bao' paddy.   When Ahu paddy is damaged by flood, 'Bao' paddy takes over and is harvested in November or December. Otherwise ibth the paddy crops   are successfully harvested. Where the depth of water is shallow 'Asra' paddy is chosen as the companion crop. Suitable 'Asra" paddy varieties like Saila Badai', 'Dhala Badal' etc., are popular. For 'Bao' paddy, varieties like 'Kekoa Bao', 'Negheri  Bao'  etc., are recommended.   Nevertheless, the modern technology of paddy cultivation has- not yet   benefited   the   deep   water  paddy   culture   and there    is no break through yet is deep water paddy cultivation.   More intensive research has to be undertaken on deep water paddy. 3.13 However, an alternate pathway to improve production  from   such   land  would  warrant   systematic development of deeper areas as organised water bodies for acquaculture and use the same water as supplementary irrigation source for intensifying crop production in the remaining peripheral areas when properly drained. Recognising its merit, the Committee considers it would be worthwhile to test the economic viability of this concept by undertaking a few operational pilot projects in the State before its large scale adoption.

# WEST BENGAL

3.14 In the 1971-78 block years, the cropped area affected by flood has been an annual average  of about 4.66  lakh  hectares.   During  the  same  period,     the maximum cropped area affected by flood in a year has also been stated to be as high as 13.3 lakh hectares. These   are indeed, extensive crop areas affected by annual floods which cause heavy loss.

3.15 In recognition of the annual flood    problem, the State  Department  generally keeps  ready     with contingent  or  alternate  croping     plan.   The     State advocates the strategy of raising of short    duration varieties of maize, jute (Corchorus capsularis),    till, mung etc. early enough so as to harvest the crop before flood.    Also community nurseries are organised to keep seedlings of paddy varieties (like IR-20, IR-26, 1R-30, NC-1281 etc.) ready for transplanting in flood affected areas when water recedes by July or before the end of August    For September floods, late transplanting has been recommended with overaged seedlings (60-80 days old)   of paddy varieties like Jagan-nath, CR-1014 etc.  which are harvested with good yields at the end of December.   Alternately short duration black gram  and mustard  are raised     before seeding the irrigated wheat variety of Sonalika. However, after October floods raising of irrigated wheat, unirrigated    gram,    lentil    or    oilseed    as    suitable to the locality is suggested. In view of their merit, our Committee endorses these contingent crop plans and alternate cropping. 3.16 in recent years, where irrigation is available, cultivation    of summer paddy (Boro), followed    by wheat in 'Rabi' is increasingly gaining popularity in the   State.     As a result, there is a demand now for more  shallow  tubewells,  low lift points  etc.   With availability   of  irrigation  water,  profitable  vegetable cultivation will also benefit the farmers.   Hence, the Committee supports such a cropping strategy    with irrigation in the unprotected flood prone areas.

# ORISSA

3.17 The coastal    deltas of    the river    basins of Mahanadi, Brahani, Baitarani and Subarnarekha experience recurring flood, water logging and saline inundation!   In    consequence,    extensive crop areas are damaged in the coastal districts of Puri, Cuttak   and Balasore.   According  to   the  crop   damage  analysis . made by the National Commission on Flood for the period  1955-70, on the average, the affected     crop area accounted for about 40 per cent of the State's total area, annually affected by flood. However, during the seventies this figure has since gone upto 54 par cent.    Hence  the  Committee  urges  the  restructuring of the cropping during flood free months for flood prone . coastal Orissa.    It is, however, hoped that the future programmes envisaged for a dam at Bhimkund {Orissa) in the Baitarni basin and at Chandil (Bihar) in the Subarnarekha basin, will substantially moderate flood and reduce flood damage in the north eastern parts of coastal Orissa. 3.18 In general, agriculture in Orissa,   means raising of paddy.   It occupies more than 70 per cent of all cropped area in the State.    In the coastal areas, paddy  is virtually the -only crop grown in 'Kharif (June-January),  which     corresponds to     Soufh-West Monsoon as also the major flood period in the State. In its report, the National Commission on Agriculture has dealt in detail with the statistics of rice production according to seasons.   It has been identified that three crops of paddy are raised in Orissa during the period namely (i) February-May, (ii) June-September,    and (iii) October-January.   Their comparative spread and yield in the State is given below: —

| Area and yield levels of paddy in Orissa* |
| --- |
| Season (based on sowing period) | Area as per cent of State's paddy area | YieId |
|  |  | As per cent of all India Yield | As per cent of overall State Yield of Orissa |
| 1 | 2 | 3 | 4 |
| February-May | 12 | 49 | 60 |
| June-September | 83 | 80 | 98 |
| October- January | 5 | 198 | 241 |

The  above  data clearly brings  out that the performance of paddy sown in February-May and    in June-September is poor.    Former suffers from moisture stress and rains at harvest while the latter    is affected  by  flood.   The  October- January  sown crop of paddy, though covers only upto 5 per cent of the State's paddy  area,  is  practically free from     flood and  performs best.      The season is     comparatively cloudless  and favours  increased photo- synthetic  efficiency for better yields.   Given the irrigation facilities from November onwards, all efforts should    be trade to expand paddy area in the October- January season.   The Committee advocates    this strategy in tr e flocd prone coastal of Orissa.

3.19 The cropping strategy for the flood prone coastal Orissa may follow similar lines as advocated earlier.   Using  suitable  crops  and  varieties     available tcday, a cropping plan to intensify production in flood free months, or to escape flood damage, has to    be developed.    As earlier advocated, the success of such a strategy depends on the availability    of irrigation water.   The   Committee,   therefore,     reiterates     its recommendations   that  immediate steps  should     be taken to increase irrigation facilities in the flood prone areas.   Given the irrigation facilities, we advocate for July-August flood prone situations early jute followed by  paddy  from  October  to  December.     After the paddy crop, a short duration 'Rabi' crop of pulses or oilseeds may be chosen.    If floods occur in Septem- , ber and October, damaging the standing rice, 'Rabi' crops  like wheat,  groundnut or soyabeen     may be raised with irrigation while under irrigated conditions alternate crops  like  sesamum, mustard,    rape, line-seed may be chosen. In the saline coastal areas, paddy is the main 'kharif crop and salt tolerant varieties like  Hamilton,  Getu  etc., are  advocated for highly saline  conditions.      In moderate  saline     situations. paddy varieties  like Patnai-23,     OC-1391,  SR-26-B, Kumangore  etc., are  recommended.

# Crop research and deep water paddy

3.20 Intensive research, carried out in the country by the scientists of the Central Rice Research Institute, Cuttak,    Agriculture   Universities   etc., and elsewhere on paddy, now offers newer varieties and technology suitable for flood prone areas. Photo-Senstitive high yielding varieties like CR-1009, CR-1011, CR-1018.     Pankaj  and Jagannath can successfully     be grown in rainfed, shallow and intermediate    waterlogged areas (15-50 cm water depth).    For recurrent flood  areas,  flood     resistant     varieties like FRG-7, FRG-8,   BR-13,   BR-14,   FR13A   and   FR-43B are recommended.   Where   semideep   (50-100 cm)   flood water  conditions  are  experienced, rice varieties  like CR-1030, CR-260-30, CR-260-31 etc.   would be   _the suitable varieties.   Floating rice .varieties like Jaisu-ria, CNDW 332, 327, 326 and 325 have shown great ecological adaptability and are recommended for deep water areas.

3.21 In short, it may be stated that suitable crop varieties are available "today.   The Committee advocates the restructuring of the cropping, which can escape or tolerate flood damage in the    flood    prone areas.   For popularising such a cropping strategy, _it is reiterated that steps should be taken to make available irrigation facilities in such areas.

3.22 Deep water  situations  occupy large areas in chronically flood prone tracts of Uttar Pradesh, Bihar, West Bengal, Assam and Orissa.   Some 2-3 million hectares acfount for such areas, where local farmers raise deep water paddy  or floating paddy.   Almost 25 per cent of these areas experience deep water conditions, mere than 50 cm  water depth.   In rest of the areas water depth is Jess than 50 cm.    Due to management difficulties, deep water paddy produces low grain yields    ranging from 0.5 to 1 tonne per hectare.   Such factors as (i) dependence on monsoons, (ii) low yield potentials of local varieties, (iii) grain shattering  habit  of varieties, (iv) poor management practices  including pest management  are  a few  of the major production constraints, responsible for low yields of this crop. Scientific research works carried out so far have been mostly in the field of varietal improvement.   As a result, a number of improved varieties are now available like (a) BR-14, BR-15, BR-46 for deep v/ater situations in Bihar and (b) for    shallow water or water logged conditions, latisal, Patnai-23 in West Bengal, Manoharsali in Assam and T-141    in Orissa are popular, varieties like FR-13-A, FR-43-B of Orissa (in Bihar BR-13 and BR-49) are reported to withstand complete submergence upto 10 days.    However, in the Gangetic plains, there are situations where paddy crop remains submerged about 20 days during the flood season of July-September.   Suitable varieties are to be evolved to tolerate long periods of complete submergence under these conditions.    Some    of the crosses involving   semidwarf   varieties   and local floating paddy have yielded promising results    with 15-50 per cent increase in yield.    Nevertheless there   appears no break through in deep water paddy cultivation.    In view of the importance of deep water paddy in the flood prone areas and the formidable problems faced for attaining any break through in    its production, the Committee strongly advocates intensification of scientific research on deep water paddy on priority basis.

# 4. IRRIGATION STRATEGY

The chapter on cropping strategy    for chronically Hood-prone areas already described the different types of cropping patterns to be adopted in such areas. It • has been suggested that by and large this strategy for such areas should be for flood escaping or flood tolerant cropping systems and intensifying crop production with irrigation in flood free months.

4.2 Chronically good-prone areas have been defined as areas having (i) flood frequency of at least once in three years (ii) flood duration of about seven days period at a stretch (ill) flood depth of more    than the standing paddy at that time and (iv) flash floods with strong current liable to uproot the plants even if the duration is less than seven days.

4.3 Even-though     flood-prone     areas in     different States have been, broadly identified, the arias    which are chronically affected by floods have not been scientifically   demarcated.    It   is,   however,   known     that such areas lie mostly in five States of Uttar Pradesh, Bihar,   Assam,   West   Bengal   and   Orissa,    Irrigation strategy in the chronically flood areas will depend on their geographical location, and availability of water resources during the flood free months.

4.4 In the chapter on cropping strategy, the chronically    flood    affected    areas    in    different    states have been broadly indicated.      It is important    to mention   that Khadir   lands   and      diara   lands   are fairly well  identified in different     states referred to above.       Generally   such   lands     which   are  in   the vicinity of rivers have a fairly high water table and it is    possible to arrange for irrigation by    tapping ground water through wells, shallow tubewells which have  to  be  covered  or sealed during  the  monsoon season  when there  is high  flow  in  the rivers  with consequent   submergence. The  other alternative for the areas which  are in the fringes of the    dry weather flow line of the river can be irrigated    by providing river lift pumps and the distribufion    can be arranged by portable aluminium or flexible polythene pipes which can be removed before floods inundate  the  areas. In either case the pumps  and motors  have   also   to be   portable  and  have  to be removed during the high flow of the river.     In fact, to meet the requirements one set of pump   and motor can be utilised by rotation for a number of such tube-wells. Location of such tubewells have to be decided after ascertaining the area to be irrigated by each unit.     So far as the khadir lands are concerned it may be possible to provide overhaul electric   transmission lines which may not get affected during the flood season.      So far as the island diaras are concerned and the khadir areas where the submergence during flood season is high, diesel sets have to    be nreferred  even though the cost of pumping will be higher.     This is suggested because it would be very costly to take the electrical transmission lines nearer the river edge with high submergence and also across the rivers to supply power to the lands.   Also power supply  to   these  areas  tend   to  be  highly   unstable and unreliable.                                                   ,

4.5 A typical case of a large    island diara near Patna which is known as Raghopur diara is inhabited by a large population.      These    people sustain themselves  on  whatever crop they  can  grow during the flood-free season.      They have been demanding bamboo tubewells which are cheap structures so that they  could  irrigate  their lands  during  the  dry  part of the Rabi season and the summer season.      These tubewells are quite cheap to construct and with portable pump sets a number of such tubewells can be operated with  one unit of pump  set.  Similar situation  prevail  also   in other  diaras  and  similar  solutions will apply.

4.6. Apart from the khadir areas  and the island diaras there are several other pockets in the States referred to above where water stagnates in the natural  depression even  after  flood  season , for  a  long time  and no     crops are grown.      The     ch.aurs of North Bihar and the "Beels" in West Bengal are typical examples of such areas.     In earlier plan periods the  chaur     drainage  schemes were     undertaken  in North  Bihar which  provided  for drainage  channels from the chaurs to  the nearest natural stream  with anti-flood sluice provided at the outfall so that when the outfall river level drops after the monsoons the chaurs could be drained during the months of October and November to allow rabi crops to be grown in  the  areas rendered  free  from  water.      The  experience is that even though the moisture availability  is  there in the  earlier  part  of the rabi season after the drainage has been effected, once the chaurs dry up completely there is no scope to grow summer season crop.     In such areas a strategy to retain some water in the natural depressions for providing lift irrigation during the later part of the rabi season and during hot weather season should be considered.      If part of these chaurs are deepened    and isolated by  wire  netting  and  retain water, even inland fisheries and water plants which command good market can be developed.     It may also be possible to  carry canal  water for irrigating  lands     rendered floodfree during Rabi and summer seasons- if there is any major, medium or minor     surface irrigation scheme operating    in the    relatively higher areas    in the neighbourhood.      The distribution    arrangements can be made from the nearest    canal water course either through portable pipes or through underground pipe   system which   may  remain   undisturbed  during the floods.      Such irrigation will provide gravity flow to the areas rendered free from floods for Rabi   and hot weather . crops in and around natural depressions. Drip irrigation with portable polythene pipes through which water could be pumped during the   Rabi Season and hot weather season would also be suitable for proper distribution of water.      Portable    sets of aluminium pipes with fittings for sprinkler   irrigation which are readily available could also be tried    with economy   in   the   distribution   and  consumption      of water.

4.7 Wells could be  sunk in the  areas which  are rendered flood-free after the monsoon months   which should be normally covered during the period of submergence and can be used for irrigation purposes with manual or animal operated devices as well as with portable  pump  sets  to lift water     from  the  wells. The covering of the mouth of the wells is necessary to prevent chokage during submergence in areas where it would not be possible to build the structure    of the well with crest above the flood level.

4.8 In West Bengal many channels keep on flowing after  the monsoon season  even  after the lands are rendered flood free.     To raise boro paddy or wheat the farmers are used to put up kucha bundhs   across the flowing channels to impound water and lift the same for irrigating the areas.    The system is    very crude and adversely affects the regimes of the natural streams or the drainage channels.     Instead of putting up, temporary earthen bundhs, if a systematic programme of construction of sluices    with    gates are drawn up and construction undertaken, perhaps    the purpose will be better achieved and during   the monsoon season the gates can be kept opened to    allow flood water to pass freely.

4.9 In Assam there are many small tributaries    of the Bramhaputra which    carry perennial    flow.    A system   of lifting water during the Rabi and summer season is already in vogue in some parts of the State. This programme should be accelerated.

4.10 As has been stated in the chapter on cropping strategy for chronically flood affected areas, in Orissa the coastal deltas of Mahanadi, Brhamani, Baitarani and Subarnarekha experience recurring floods, water logging and saline innundation. Principal crop grown during Rabi and hot weather seasons is paddy but there is need for irrigation. They hydrogeological studies have revealed that good quality ground water is available at varying depths which can be harnessed    mostly -through deep tube wells.     These can also be provided with portable pumpsets and distribution pipes.

The latter may also be underground    concrete pipes with outlet valves which can be closed during   flood season.      The  well  mouths have also to  be sealed during floods, wherever scope exists the same    may be tried.   The  inland low    lying areas which    get water-logged  during  monsoon  season can  also     be - tackled in the manner to be adopted    for chaurs in North Bihar.

4.11 In  some  flood affected  areas  in these States there are abandoned river    channels  where     water accumulates during the monsoon season which    can be harnessed through lift pump for the purposes of irrigation during the flood free months.

4.12 So far as areas subjected to flash floods    are concerned, the same strategy of tube wells, wells and river  lifts  can  be considered  with   similar   portable arrangements  for   pumps,   motors  and      distribution system  for providing irrigation  during     Rabi     and hot-weather seasons. In such  areas it  is not advisable not to try any crops during, flood periods.

4.13 Farmers in  the   chronically     flood   affected areas  are  generally   economically  weak     and  it  is important that they are provided with necessary   credit facilities (long, medium and short term)    to enable them to go in for irrigation arrangements    of the type suited to a particular situation   and also to procure    other    essential    inputs.       Subsidies    for small /marginal farmers would be desirable. State responsibility  for     supporting     small  farmers     for minor irrigation should be there.

4.14 The   strategy   of adopting  suitable cropping pattern coupled with provision of irrigation facilities and other essential inputs will lead to utilisation of extensive areas which mostly remain fallow even after the  floods have  receded.      And     even where crops are grown the yield is very low due to lack of moisture.

5. MEASURES TO MITIGATE FLOOD   DAMAGES

5.1 It is fully realised that absolute immunity from flood  damage is not physically possible even in the distant future because of unpredictability    of several natural forces which might cause unprecedented situation.      Even  so,  with  proper  planning  and  continuous  effort we can certainly look forward to     an appreciable  diminution     of distress with an accelerated implementation of flood management measures.

5.2 The  Committee  has already   stressed  that   the measures to mitigate flood losses need to be part of a   comprehensive  scheme   wherein   modifications     of floods,  reduction  of  damage   susceptibilities     to  infrastructure and  property and bearing     the loss are looked   at   in   an   integrated   fashion.       These   have been viewed  mainly as physical methods of protection  from floods.      This Committee agrees with the suggestions of  the R.B.A.  (Rashtriya     Barh  Ayog) that  all   types of  measures,     physical  or  otherwise, have to    be    considered    for    flood    management. These may comprise physical, biological,    economic, social and administrative     such  as soil conservation and  afforestation reservoirs,  embankments,     drainage channels,  dredging,     flood  plain regulatories,     floocl forecasting and warnings,    emergency    measures etc. The Rashtriya Barh Ayog report has given comprehensive   treatment to   engineering   and   other  aspects of flooding  whereas  the  prime concern of the  present report is with the aspects affecting    the chronically  flood  affected     areas only.        Broad endorsement   of the relevant recommendations   of the R.B.A. is there and wherever necessary modifications and additional recommendations have been highlighted.

Upper Reaches Control

5.3 There    has been a    controversy as to whether watershed   management (sometimes described as flood abatement) or flood protection    is the more efficient adjustment to floods.      This has come to be referred to as the "up-stream & down-stream" controversy or the conflict between "big dams and little dams". On the one side are those who argue that the best way to deal with floods is to control them,    where they form.   They  suggest  that  deforestation  and     deve-getation are major causes of floods and so the most appropriate course of action is to plant trees in the place of those that have been cut down, to improve vegetative  cover  in  areas  subject to  soil        erosion and to  phase out farming practices    that contribute to sucn erosion.     They see dams   as a means of controlling run-off but feel thai these are most effective in the headwaters rather those down-streams      They point  out further   in  this connection that   up-stream reservoirs are less likely    to take out of production agricultural land or forest land.     On  the other side are those who believe that the most efficient way to deal with floods is to control these where they are likely to do most damage.      They point out that it takes several small reservoirs in the up-stream region to do the work that one large reservoir further downstream may do.     They also argue that the contribution of programmes of reforestation and   conservation to  run-off control  may  be  insufficient  to  deal  with flood problems.      Big .dams and various down-stream control works are seen as more effective alternatives. This Committee feels that Flood abatement measures up-stream and control measures down-stream are not necessarily alternatives.    These should be considered as complementary components   of an overall programme  adjustments to  floods.       A typical     case relating to Howai River Basin is given in Annexure 5.1.

5.4 In India the overall storage    capacity created m all the river basins, as    indicated by the R B A. accounts for hardly a tenth of the    average annual flow.     In terms of utilisable quantity of surface water resources, the per cent utilisation is estimated to    be nearly a fourth.

5.5 Moderation   of   spectacular  variations     in  the flow of water, can be had through the increasing provisions of storage in natural lakes, artificial reservoirs, sou mantle and underground acquifers.

5.6 Erosion causes destruction of fertile land. Torrents    get widened over time and through damaging or eroding fertile land affect the streams as well as reservoirs adversely due to much of silt inflow.     Satellite photographs and     available    topographic maps have been utilised to study the widening of torrents in the shivalik range in U.P. The data gathered for four point times and different  rows in  the   interval of seven years shows an overall average 15 per cent increase in the width of rows.     The satellite photographs were taken on the  14th of November   1972, 8th of May, 1974,   13th of April, 1977 and on 21st of April,  1979.      The details of the estimated measure width are indicated in the following table: -

| Table : Estimated measured width {in in eters) at the level of 1972 |
| --- |
| Name of row | 14-11-72 | 8-5-74 | Annual increase from 72 to 74 | 13-4-77 | Annual increase from 74 to 77 | 21-4-79 | Annual increase from 77 to 79 | %of increas; of width in 7 years | %of annual increass |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| Badhsahi bagh | 125 | 150 | 10 | 225 | 17 | 300 | 17 | 140 | 20 |
| Badkela | 500 | 750 | 25 | 875 | 6 | 1000 | 7 | 100 | 14 |
| Shakumbhari | 450 | 500 | 5 | 600 | 6 | 775 | 15 | 70 | 10 |
| Khaianavar | 375 | 550 | 23 | 775 | 14 | 875 | 6 | 134 | 19 |
| Mohand | 125 | 225 | 40 | 250 | 4 | 300 |  | 140 | 20 |
| Total | 1575 | 2175 | 19 | 2725 | 12 | 3250 | 9 | 106 | 15% |
| Source : Data worked out by Shri P.N. Gupta, Project Director, Land Survey Directorate, Uttar Pradesh . |

5.7 Generally   the   satellite   photograph   is      about 80   X   80 metres and as such may not     yield very precise idea of the measurement.     Talcing full account .of such like aspects it may be said that the width would not increase by less than 10 per cent per year. The  impact  of  such  denudation on  adjoining  areas can well be realised.

5.8 The Committee would like to recommend   that full potential of the Landstat' Imagery be utilised    to know precise details is about the behaviour of various upper reaches in the country.      This technique provides  a  greater degree  of flexibility  than  the  maps obtained  from   traditional     sources     Aerial  photographs afford this possibility but in that case a much larger number of prints have to be handled   and transfer of interpreted details on to maps for terrain with extremes of altitudinal variations is a problem. Small scale  maps  with  full   details  of  river systems and with so much of accuracy are extremely difficult,    if not   impossible,   to  gel by  another  method.

5.9 Expert   handling   of   interpretation   and      map making  from  the  imagery alongwit'n   survey in conjunction  with photo interpretation of aerial photographs,   can greatly  facilitate   in  the  preparation  of actual     a forestation  and     watershed     management plans. The Committee recommends that full potential of the repetitive imagery data be exploited    by analysing the same with the aid of electronic computer.   Along    side the inherent knowledge    about the local conditions would greatly facilitate in carrying out. the  whole  process  efficiently     and  expeditiously towards the good of the community welfare.

5.10 The availability of data about the    effect    of soil conservation measures is rather very limited    in  character.   However,   even   that  limited     data     do provide some useful clues.   The data, already quoted by the R.B.A.. is given in the table that    follows:

| Table- Effect of soil conservation measures or. sediment discharge in Bhakrand Ramganga basins* |
| --- |
| Reservoir | Catchments area (000 ha) | Sediment yield (ha. m/ 100 Sq.Km) |
|  | Critical | Treated | %of critical area treated | Assumed | Original | Observed | % reduction |
| Bhakra | 557 | 126 | 23 | 4.3 | 6.9 | 5.2 | 2.5 |
| Ramganga | 104 | 42 | 40 | 4.3 | 22.0 | 16.8 | 2.3 |
| *Source:Tecd. Bull, Soil & Water Conservation in the catchments of river valley projects, Soil Cons. Dts.CWC: (G.P. Gupta). |

5.11 The  above     figures  show  very     conclusively the   desired   effect   of   soil      conservation  measures. Specially in the case of Ramganga one notices    that 40 per cent of the critical area got    treated leading to 23 per cent    reduction in sediment yield.        The committee would like to recommend and emphasise the importance of  undertaking extensive soil conservation measures.      These measures of providing vegetative and forestry cover to help in modifying    the floods and controlling the run-off.      The moderation of run-off would directly help the chronically flood affected areas.      For reduction   of run-off,   the Committee would also like    to recommend (i) prohibition of production in the hilly catchment; (ii) contour bunding in hilly catchment; (iii) construction    of flood detention reservoirs; (iv) small check dams    on the tributaries to delay run-off to point of concentration; and (v) elaborate arrangement for flood fighting   arrangements at vulnerable points with adequate support of flood forecasting and warning thereof.

5.12 Some steps have been taken towards afforestation,  though  much  more  needs to  be done     to arrest the trend towards denudation and to reforest these areas.      Intensification    of these measures will serve to reduce the amount of sediment entering    the river systems.      Part of the afforestation drive should be devoted to horticulture   at suitable   lower altitude, fruit orchards could not only arrest erosion    of soil but also provide livelihood to many.

5.13  The Committee would recommend the construction of a number of smaller flood retention re servoirs of suitable capacity on or near each river, by excavation if necessary.      This will serve to regulate the ferocity of flash floods down-stream    of these reservoirs.      The retained flood waters in various    reservoirs   can provide   ample water supply   during the dry season. Discharges    from these flood    retention reservoirs  can  also  be  used for  power     generation using low-head  water turbines, the water in the tail races being used to augment the levels    in the river or remote reservoirs as required.

5.14 The   upper reaches     management  can   be  most effective on a watershed management basis.      However, at times a judicious choice between conflicting alternatives has  to be made. For instance, watershed may serve either for low flow augmentation or flood reduction.      Rarely both the aims can be satisfied simultaneously and a decision regarding   the importance of one or the other has to be made in a given situation.     The challenge can be rightly met by deciding about the trade-off, between the two alternatives, through the technique of cost benefit analysis.

5.15 Any individualistic   attempts at soil   conservation  measures  may  not yield the  effective     results. The whole watershed needs tackling in    totality   by the Governments and the individual farmers    should be made to work within the prescribed    norms.      In consonance with the overall objectives, any financial needs of the individual farmers should be satisfactorily backed by governmental agencies.

5.16 Watershed measures can serve as a useful complement  to the protective measures to be    adopted lower down the stream.      Besides, it would    help in encouraging the increasing   use of flood-prone   areas. Herein, the Committee would like  to recommend that the programme, like that in case of flood protection, need to encompass the measures which    temper increases in the flood loss potential.

# Maintenance of Embankments

5.17 Embankment  construction     has been one of the age old method of reducing flooding.     The  Committee agree that the object of remedial measures of the protection of a chronically flood affected    area should be to train the rivers on their way to the sea by constructing   protective    embankments,   judicious drudging flood escapes etc.    After   the    devastating floods of 1954 about 10,000 km. of embankments have been stabilised (covered up) in various river   basins in the country. While these have been providing reasonable protection to large population, breaches have been too many causing severe damages to the areas in the neighbourhood.     One of the main reasons attributed to such frequent breaches has been found to be inadequate maintenance.      The Vllth Finance    Commission had gone into this question and had made the following recommendation which this Committee fully endorses.

"The Department of Irrigation have indicated that in the last couple of decades, the funds provided for the maintenance of flood control works in most States were inadequate, with the consequence that   embankments breached often, leading to substantial   damage to life and property, and also to large expenditures on repairs and restorations of the works, rehabilitation of the people affected, etc.     Ministers'     Com mittee  which  reported  in March,   1972 had  recommended  that the  annual  provision  for  maintenance of embankments and drainage works   should be 4 to 5 per cent of the capital cost worked out to the price levels of 1972, and 5 to 13 per cent in the case of river-training and   anti-sea  erosion   works.         That Committee found that in fact about 0.5 per cent of the capital cost was being then spent on the whole for maintenance of these works.       The Sixth Commission provided 4 per cent of the capital invested at the end of 1973-74 for the maintenance expenditure for flood control works.     The Central   Water Commission have now stated in a communication to us that there are about 10700 km. of embankments and 18700 km.    of drainage    channels constructed    till March, 1978, apart from anti-sea erosion works and river training works.     They have indicated  the norms of  maintenance  expenditure for  different kinds     of works,    observing    that a uniform percentage of the capital cost would not be appropriate.     The Department have suagested that earthen embankments would need  between Rs.  7,000 and  Rs.   10,000 per     km. annually at current price levels during the first 3 years and between Rs. 5,000 and Rs. 7,000 thereafter.   On current costs of    construction     the Department has worked out that these norms would be 3 per cent of the  capital  cost  initially  and  2  per  cent thereafter. Armoured embankments are stated to require   annua-ally from Rs. 5,000 to Rs. 7,000 per km. For drains, broadly classified into three categories by capacity, the norms of maintenance suggested by the Department are Rs. 1,000 per km. (upto 200 cusecs capacity), Rs. 1 ,500 per km. (upto 500 cusecs capacity) and Rs. 3,000 per km. for capacities    above 500 cusecs.   On    the basis of these norms, the Department    have roughly estimated that the annual maintenance costs     would be Rs. 15 crores for all flood protection   works in the country.     The actual expenditure as seen    from the accounts, was over Rs. 2J crores in 1976-77, but this figure  probably  includes special  repairs  as well  as reconstruction after damage by floods, which are not included in the calculation of the annual costs done by the Department.

In the light of the above, we have estimated the annual requirements for maintenance of flood control and  drainage  works,   and  anti-sea erosion     works, taking into account the physical  data from the Central Water Commission and the States, the maintenance norms suggested by the Department of Irrigation, the actual expenditure in each    State in  1976-77,    and such data as are available in the budget documents and the finances accounts of the States".

# Drainage

5.18 Properly maintained drainage system can help to reduce the intensity and duration" of   flooding considerably.      At times  the  improper  and inadequate maintenance of the channels  gets aggravated     with the presence of obstacles in the nature    of embankments on roads, railways and canals   and the people's indiscipline.     The importance of preparing a comprehensive plan of action, as already emphasised, assumes greater strength in the context of drainage management.     The Committee would   like to emphasise involvement of all the  concerned     authorities/agency which would be responsible   for clearing   all construction works in the flood plain areas and would thus avoid cross-purpose strategies.

5.19 The  Committee  would  like  to  highlight the maintenance of drainage by dredging     and utilisation of the material thus dredged   for filling   up the hollow areas on the other side of the embankments. It would also like to recommend that the maintenance of major/medium drainages wherever maintained   by Revenue  Department, must be     taken over by the Irrigation Department.

5.20 The  Committee,  while  endorsing  the     comprehensive treatment of the subject by the  R.B.A., would like to re-emphasise and recommend the following measures: —

1. There is need for closer coordination   amongst concerned agencies   like the Railways, National Highways, State Irrigation /Flood Control Departments so as to ensure that   structures   like bridges, roads, railways etc.     do not aggravate flood problems.

2. Prior consultation by National Highway authorities, State P.W.Ds and Railways     with the State   Irrigation /Flood   Control     Departments should  be made obligatory.         To  facilitate an expeditious    check,      the Government    of India   should      evolve     a   guideline /checklist for the purpose of vetting   of waterways by the State  Irrigation /Flood  Control     Departments.

3. It. should be mandatory   that assessment of adequacy of existing waterways   should   be made by the State Committee of Engineers or some other Technical    Board and the waterways for bridges to be constructed in the future should be vetted by the State Irrigation /Flood Control Department.

4. The Standing    Committee for settling disputes on waterways and sharing of costs, headed by the Chairman, Central Commission, should be vested with statutory powers for implementation of its decisions.

5. The State should   undertake legislation   to prevent unauthorised river bed cultivation     and encroachments into drains etc., and where such laws   already   exist,   the   enforcement   agencies should be strengthened.     Cultivation   of crops like water-melons, vegetables, etc. in river beds and  berms,  may  however,  be  allowed     with caution.      The practice of cultivation    in the abandoned    beds    of Dhars which    discharge into main rivers should be stopped.

6. Where suitable legislation with a penal clause for unauthorised crossings over drains has not been enacted, the same should be done    and enforced.

The  Committee  would  recommend  that  Hood relief channels should be constructed   at suitable   points to *drain excess of flood water to remote   artificial lakes; these should also be provided towards the downstream end of enlarged channels to carry away surplus  water to  other artificial  lakes.  The flood relief     channels can be used as feeders for minor irrigation canals.

Sanding /Silting

5.21 Chronic floods, quite    apart from causing the loss of life and property, carry heavily   siltladen water down to the estuaries.    The silt, instead of being a most useful — agent in soil fertilisation merely    serves to clog the water channels.

5.22 The amount of sediment /silt in certain   basins is quite high and its entrapment and removal has not been attempted to any significant length and the resultant benefits have not been availed of in the process.

5.23 Embankments are provided with sluices opening both ways.   These are to drain out water from the countryside to the natural stream where the water level of the latter so permits.   The other purpose contemplated was to let in some silt laden water in a controlled way to the countryside to provide fertilising silt and also    to maintain continuity in the natural land building process, though in a somewhat limited manner.   Unfortunately these sluices have not functioned properly and there are no foolproof methods laid down for operation of these sluices to serve both the purposes.    The Committee would recommend a complete review of the operation of these systems of sluices for drawing up a necessary operational manual for the same.

5.24 In the absence of objective data on the behaviour of river beds during and after floods conclusive ideas on the subject are rather difficult to form.    To get some concrete ideas about the problem the Committee got a study through the Government of Orissa. The study has been confined to the Mahanadi, Katha-jori,  Kuakhai  and  Surva rivers  and  has  considered comparable  eleven  cross-sectional  points.   The  data reveals practically stability of bed levels.   The details of the exercise can be seen from the following table: —

Generalising   the   behaviour     of  river  beds   from above would be rather risky and the Committee would recommend the  undertaking  of  similar exercises for the various river systems so as to have an in-depth understanding of the problem. Such    an understanding would greatly help in devising judicious remedial measures.

5.25 During high floods the spillage of water over the banks sometimes creates the problem    of sand casting in the agricultural fields.   The paucity of data inhibits in making any objective ideas about   the problem.   The  Committee  would like  to     recommend undertaking   of   studies   whereby   assessment   of   the problem in the right perspective can be had.

5.26 The problem of sand casting, beyond a limit, is quite harmful for the crop growth.    The Committee would recommend the initiation of scientific studies on the subject so that suitable crop planning can be devised.

Protection of Human Settlements

5.27 Floods in their wake even with low intensity, cause intolerable distress for the human settlements and more so in rural areas.   The houses get damaged as these generally lack a strong ground floor structure and also do not have a high foundation.

5.28 To ward off the ill effects to human settlements, strengthening of house structures, raising the level of the whole villages or ring bunds around villages have been  considered  as  the  possible  alternatives.   Each of these alternatives have their positive and negative aspects.

5.29 The rural houses, facing flood fury, are generally   made   of   materials   which   cannot   withstand greater degree of stresses and strains.   In the event of raising pucca structures the damage susceptibility can be considerably reduced. But the great majority of the owners of these houses belong to the poorer sections of the society and cannot afford the needed cost.    A single pucca room with a loft or with an additional room on the first floor of each house can save   the   inhabitants  from  shifting  during   flooding. Even the affording of this much cost appears to    be beyond the means of the significant segment of the affected lot.    Left to the natural play of forces implementation of such like ideas are not likely to materialise in foreseeable future.   The alternative appears, to be in provision of public funds for achieving the desired ends.    Considering the magnitude of the problem in the areas liable to normal flooding, the whole proposition does not seem to be feasible.      However, in case of chronically flood affected areas the magnitude of the problem might be in the realm of practicability and hence adoption.    The Committee would like to support such a scheme in areas where alternatives are not  found  to  be  feasible.   In case  of its adoption 'strict enforcement would be desirable as otherwise additional numbers in the hope of receiving doles for construction may get settled in affected areas.

5.30 Raising of villages as a whole offers another alternative to mitigate the hardships of human settlements.    Raising the present site of the village is not feasible straightaway without wholesale demolition of the  existing  structures.       Moving  the  whole  village to a new higher site would involve construction    of "new   structures   altogether.    Without   liberal   support from public funds the proposition can rarely succeed.

5.31 Some inherent contraditions have been noticed wherever the scheme of village raising has    been attempted.    Generally with the raising of -the villages, roads etc. have been raised as well and no    proper allowance for drainages etc.   has been made.    This has rather led to aggravation of the flood situation.' The Committee would recommend that in- case of raising of villages, roads should not be raised correspondingly so as to avoid any interference with drainage aspects. The roads may be allowed to get submerged during floods.    Availability  of  country  boats   in     sufficient numbers would be able to solve the problems, of the chronically  flood  affected   areas during  that spell.

5.32 Construction of ring bunds around the villages or human settlements is another way which has   been experimented   at  certain   places.   The  major drawback of the scheme has been noticed in the draining out of the water from within the settlements.    Pumping out the water has been visualised as one of the possibilities.    The Committee would support such    a scheme in the even cost-benefit favouring the same in  comparison  to  other alternatives.   The  Planning Commission had suggested that instead of putting up raised platforms to provide shelter for people living in villages which get marooned during floods resulting in loss of human lives, and who also get affected by various types of epidemics during the post flood period, it is preferable to excavate tanks at suitable points in the villages, utilise the excavated earth in putting up embankments   all   around   sufficiently   wide   to   provide shelter to the marooned villages. At the same    time the tanks so formed would collect good water from rains and provide the villages with safe drinking water during floods when water all around get pulluted.

5.33 The Committee would recommend that structural, changes and land elevation wherever undertaken by individuals or groups, should be encouraged and suitable monetary  and  other assistance be provided keeping in view the overall policy objectives.        It is well recognised that structural changes and    land elevation for human settlements do tend to encourage persistent occupancy of chronic flood affected areas. At the same time they do offer, however, a means of reducing potential losses and they do place part of the burden on the flood plain occupants.

5.34 The  Committee  would   recommend   strict  regulation of land use in the chronically   flood affected areas.   Such a measure brings in its fold some distinct advantages.    The most important among them being that it encourages careful weighing of the costs against the benefits of flood plain occupancy.    Along side it forces  consideration   of the relative   advantages     of being in the flood plain as against the location elsewhere and leads to a valuable complement of other types of adjustments in the nature of emergency action, flood-proofing,  structural changes  and flood control, The Planning Commission has already provided    for soil conservation  and  afforestation  measures in  the upper catchment of flood prone rivers in the    Sixth Five   Plan   (1980-85).    This   programme  will   require to be implemented on sub-watershed basins after identifying  the  critically  affected   ones,    Effective  implementation of this programme will require building of inter-disciplinary teams, for each of the basins. The pace of the programme will have to be accelerated along with effective measures to prevent deterioration of new areas. The Committee would recommend special efforts in this direction.

5.35 One of the approaches to the management of flood losses can be through modification of the incidence of burden.   This can be achieved either    by spreading it over a larger segment of the society than that is immediately affected or by spreading it more evenly over time.   The modes of such measures could be through disaster relief, land revenues exemptions and other taxes, write-offs and other emergency measures.   In all these measures naturally governmental role has to be of prime importance.   Disaster relief, while warding off the immediate distress, encourages certain attitudes which need to be deplored.   There is a tendency to consider relief measures as a right rather than a charitable gift.    This in turn tends to remove the incentive to avoid future flood losses and encourages persistent human occupancy of the flood plain. The Committee would recommend that effective measures in that direction need to be comprehended.

5.36 Effective steps should be taken to train    and organise local volunteers in fighting flood hazards due to threatened breaches in embankments and also to utilise effective steps to plug the breaches as and when the same occur.

5.37 On account of pressure of population it may not be possible to totally prevent flood plain occupancy even if there be a legislation for the same but    the Committee feel that there should be a law to ensure that any building that is constructed should provide for a plinth above the normal flood level.   In   such areas    provision    of boats is a must to enable the marooned  people   to   maintain   communication   with the unaffected areas.

Sd/- B. SIVARAMAN, }
Chairman.

NEW DELHI, 
12th November, 1981.

| COMPARATIVE STUDY OF CHANGES IN BED OF MAHANADI RIVER SYSTEM FROM NARA.I TO JOBRA WEIR AND NARAJ TO OFF TAKE SAURA (FROM 1899 TO 1979) |
| --- |
| Name of River No. | Cross Section No. | Location of Cross Section | Year | Average river level in ft. | Year | Average river level of bed in ft. | Rise or fall | Remarks |
| 1. Mahanadi River | 1 M. | At 2604 ft. U/S (Along River Course) of Jobra Weir | 1899-1900 | 62.05 | 1971-72 | 61.55 | Fall in 1971—72 | 0.50 ft. |
| 2. Do. | 2M. | At 4950 ft. U/S (Along Course) of Jobra Weir | 1899-1900 | 65.03 | 1971-72 | 66.67 | Rise in 1971—72 | 1.59 ft. |
| 3. Do. | 3M. | At 12540 ft. U/S (Along Course) of Jobra Weir | 1899-1900 | 66.91 | 1971-72 | 67.26 | Rise in 1971—72 | 0.35 ft. |
| 4. Do. | 4M. | At 32340 ft. U/S (Along Courss) of Jobra Weir | 1899-1900 | 70.23 | 1971-72 | 71.15 | Rise in 1971—72 | 0.92 ft. |
| 5. Do. | 5M. | At left end of Naraj Weir | 1899-1900 | 74.17 | 1971-72 | 67.08 | Fall in 1971—72 | 7.09 ft. |
| 6. Do. | 6M. | At right end of Naraj Weir | 1899-1900 | 59.70 | 197172 | 60.09 | Rise in 1971—72 | 0.39 ft. |
| 7. Kathajori River | 1 K. | At 4620 ft. D/'S (Along river Course) of Naraj Wur | 1899-1900 | 66.67 | 1975-76 | 75.00 | Rise in 1961—62 | 8.33 ft. |
| 8. Do. | 2K. | At 25740 ft. D/S (Along river Course) of Naraj Weir | 1899-1900 | 63.30 | 1961-62 | 64.00 | Rise in 1961—62 | 0.70 ft. |
| 9. Do. | 3 K. | At 33000 ft. D/S (Along river Course) of Naraj Weir | 1899-1900 | 64.13 | 1961-62 | 59.00 | Fall in 1961—62 | 5.13 ft. |
| 10. Kuakhai River | 4 Ku. | At 40000 ft. D/S (Along river Course) of Naraj Weir (3000 ft. inside Kaukhai) | 1961-1962 | 69.39 | 1979-80 | 70.68 | Rise in 1979—80 | 1.29 ft. |
| 11. Surua River | 5 Su | At 47800 ft. D/S (Along river Course) of Naraj Weir or (10000 ft.) D/S of Kathjori Railway bridge) (in river Surua). | 1961-1962 | 56.54 | 1978-79 | 54.00 | Fall in 1978—79 | 2.54 ft. . |

ANNEXURE 5.1

# Extracts of the report on Irrigation, Drainage and water management in China by 
Shri R,S. Saksena (pp.  14-17).

# Hwai River Basin

"The Hwai is one of the China's major rivers along with the Yanglese   and   Yellow   rivers   is   more   than      1000  km. long.      It has got 500 tributaries with an average drainage area of 100 km each".

"In the year   1931, the flood submerged 4 million ha. of farm land and affected 20 million people".

"Maximum   emphasise   was   placed   on   flood   control   for which the following steps were taken:

(i) Reservoirs were built in the upper reaches of the main tributaries — 35   big   reservoirs   and   5000  medium  and  small size reservoirs were completed with a storage of 23 x  109 M3 in  the  upper     reaches.      In  addition,     work     of afforestation and soil conservation was taken up in the areas.

(ii) In the middle reaches, the river courses were enlarged and full use was made of lowlying land for sharing the water. The  flood  deduction  so  made  had  a  storage     capacity  of 28  X   109M3.

(iii) In the lower reaches, embankments were    re-inforced and more  channels  were  dug  to provide     increased  outlet, with a  flood  discharge of 22000M3/Sec.

(iv) In coastal areas, embankments were built , dredging of channels and drains was taken up to control water   logging.      Drainage capacity was built for a standard frequency of draining 120-180 mm of rainfall in 3 days.        New channels and canals were built for reducing water logging. Out of 8.7X106 ha. of low  lying land,  it has  been possible to protect 4.7 X 106 ha. of land now, which has been transformed into paddy fields".